## Slide 1: Bits and Data Storage

## Slide 2: Basic Hardware Units of a Computer

## Slide 3: Bits and Bit Patterns
Bit: Binary Digit (0 or 1)
Bit Patterns are used to represent information.
  Numbers
  Text characters
  Images
  Sound
  And others

## Slide 4: Boolean Operations
Boolean Operation: An operation that manipulates one or more true/false values
Specific operations
  AND
  OR
  XOR (exclusive or)
  NOT

## Slide 5: The Boolean operations AND, OR, and XOR (exclusive or)

## Slide 6: Gates
Gate: A device that computes a Boolean operation
  Often implemented as (small) electronic circuits
  Provide the building blocks from which computers are constructed
  VLSI (Very Large Scale Integration)

## Slide 7: A pictorial representation of AND, OR, XOR, and NOT gates as well as their input and output values

## Slide 8: Flip-flops
Flip-flop: A circuit built from gates that can store one bit.
  One input line is used to set its stored value to 1
  One input line is used to set its stored value to 0
  While both input lines are 0, the most recently stored value is preserved

## Slide 9: A simple flip-flop circuit

## Slide 10: Setting the output of a flip-flop to 1

## Slide 11: Setting the output of a flip-flop to 1 (continued)

## Slide 12: Setting the output of a flip-flop to 1 (continued)

## Slide 13: Another way of constructing a flip-flop
** Usually abstracted out as a box that stores a bit **

## Slide 14: Main Memory Cells
Cell: A unit of main memory (typically 8 bits which is one byte)
  Most significant bit: the bit at the left (high-order) end of the conceptual row of bits in a memory cell
  Least significant bit: the bit at the right (low-order) end of the conceptual row of bits in a memory cell

## Slide 15: The organization of a byte-size memory cell

## Slide 16: Main Memory Addresses
Address: A “name” that uniquely identifies one cell in the computer’s main memory
  The names are actually numbers.
  These numbers are assigned consecutively starting at zero.
  Numbering the cells in this manner associates an order with the memory cells.

## Slide 17: Memory Terminology
Random Access Memory (RAM): Memory in which individual cells can be easily accessed in any order
Dynamic Memory (DRAM): RAM composed of volatile memory (usually when referring to RAM we mean DRAM)
Read Only Memory (ROM) : RAM that cannot store new values; limited to pre-stored data

## Slide 18: Measuring Memory Capacity
Kilobyte: 210 bytes = 1024 bytes
  Example: 3 KB = 3 times 1024 bytes
Megabyte: 220 bytes = 1,048,576 bytes
  Example: 3 MB = 3 times 1,048,576 bytes
Gigabyte: 230 bytes = 1,073,741,824 bytes
  Example: 3 GB = 3 times 1,073,741,824 bytes

## Slide 19: Mass Storage
On-line versus off-line
Typically larger than main memory
Typically less volatile than main memory
Typically slower than main memory

## Slide 20: Mass Storage Systems
Magnetic Systems
  Disk
  Tape
Optical Systems
  CD
  DVD
Flash Drives

## Slide 21: A magnetic disk storage system

## Slide 22: CD storage

## Slide 23: Files
File: A unit of data stored in mass storage system
  Fields and keyfields
Physical record versus Logical record
Buffer: A memory area used for the temporary storage of data (usually as a step in transferring the data)