## Slide 1: IP : Internet Protocol
Chapters 18,19

## Slide 2: Introduction
One key aspect of virtual network is single, uniform address format
  Can't use hardware addresses because different technologies have different address formats
  Address format must be independent of any particular hardware address format
When we address a packet
  Sending host puts destination internet address in packet
  Destination address can be interpreted by any intermediate router
  Routers examine address and forward packet on to the destination
All of these addresses are virtual; they are defined in software, not hardware

## Slide 3: TCP/IP Addresses
Addressing in TCP/IP is specified by the Internet Protocol (IP)
Each host is assigned a 32-bit number
  Called the IP address or Internet address
  Unique across entire Internet
Each IP address is divided into a prefix and a suffix
  Prefix identifies network to which computer is attached
    No two networks can be assigned the same network number
  Suffix identifies computer within that network
    No two computers on the same network can have the same suffix, but computers on different networks can have the same suffix
  Address format makes routing efficient

## Slide 4: Properties of IP Addresses
Network numbers (prefix) are unique
  Assignment of network numbers must be coordinated globally to ensure uniqueness
  Assigned by ICANN (formerly InterNIC/Network Solutions)
Host addresses (suffix) may be reused on different networks
  combination of network number prefix and host address suffix will be unique
  assignment of host addresses can be managed locally
    E.g. your ISP can set the host addresses and names within the purview of their assigned network by ICANN

## Slide 5: Designing IP
IP designers chose 32-bit addresses
  Still 32 bits in IP version 4 used today
  May cause a problem soon, not a large enough address space!
Allocate some bits for prefix, some for suffix
  Large prefix, small suffix - many networks, few hosts per network
  Small prefix, large suffix - few networks, many hosts per network
Because of variety of technologies, need to allow for both large and small networks

## Slide 6: Classful Addressing
Designers chose a compromise - multiple address formats that allow both large and small prefixes
Each format is called an address class
Class of an address is identified by first four bits

## Slide 7: Address Classes
Class A, B and C are primary classes
  Used for ordinary host addressing
  Owner of a class is assigned a prefix, gets to pick what machines they want in the suffix
  Classes A and B are all allocated!
Class D is used for multicast, a limited form of broadcast
  Internet hosts join a multicast group
  Packets are delivered to all members of group
  Routers manage delivery of single packet from source to all members of multicast group
  Used for mbone (multicast backbone)
Class E is reserved for future use

## Slide 8: Dotted Decimal Notation
Class A, B and C all break between prefix and suffix on byte boundary
Dotted decimal notation is a convention for representing 32-bit internet addresses in decimal
Convert each byte of address into decimal; display separated by periods (``dots'')

## Slide 9: Addressing at UA
The University of Alaska has a single Class B network address, 137.229.0.0
All hosts at UA have a 137.229 prefix:
  137.229.134.207 – mazzy.math.uaa.alaska.edu
  137.229.16.20 – www.uaf.alaska.edu
  137.229.150.11 – vor.uas.alaska.edu
Suffix bytes are used to determine local network and host through subnetting

## Slide 10: Address Class at a Glance
While dotted decimal makes separating network address from host address easier, determining class is not so obvious
Look at first dotted decimal number, and use this table:
Just a little binary number conversion based on first 4 bits

## Slide 11: Division of the Address Space
Classing scheme does not yield equal number of networks in each class
Class A:
  First bit must be 0
  7 remaining bits identify Class A net
  27 (= 128) possible class A nets
For the rest:
Running out of IP’s? Not allocated very efficiently
232 = ~4 billion possible hosts
But not all of the hosts being used! Some IP’s reserved too
Does UA have 65536 hosts? Stanford used to own a Class A
Solutions : Classless addressing, private address space

## Slide 12: Reserved Addresses
RFC 1597 – Address Allocation for Private Internets
  The following blocks are reserved for private internets
    10.0.0.0 - 10.255.255.255 Class A
    172.16.0.0 - 172.31.255.255 Class B
    192.168.0.0 - 192.168.255.255 Class B
    We’ll need a gateway to translate from these addresses to the Internet addresses, and we’ll examine this later… common way to connect a home network to the Internet
    We should never see a machine on the Internet with one of these network prefixes (hopefully)

## Slide 13: Classful Addressing Example
Organization with four networks, completely private network
  Assign Class A,B,C addresses as appropriate for number of hosts on each network

## Slide 14: More Special IP Addresses
Network Address
  The network itself is assigned an address
  So no host can have all zero’s as its IP address suffix
  Prefix is the network prefix, suffix is all zero’s
Directed Broadcast Address
  Broadcast message to a network
  Prefix is the network prefix, suffix is all one’s
  So no host can have all one’s as its IP address suffix
Limited Broadcast Address
  Broadcast on the local LAN
  Entire address is all 1’s, i.e. 255.255.255.255

## Slide 15: More Special IP Addresses
This Computer Address
  To obtain an address automatically when booting, we may use IP to communicate… but we don’t have a correct IP address yet
  Use an address of all zero’s to indicate “this computer”
Loopback Address
  Any address beginning with 127 indicates the local computer
  E.g. 127.0.0.1 most common, but could be 127.0.44.53
  Use for testing, no packets leave the computer

## Slide 16: Special Address Summary

## Slide 17: Subnet and Classless Addressing
Classful Addressing can be wasteful if we don’t utilize all the hosts within a network Class
Two mechanisms to overcome the limitations
  Subnetting
  Classless Addressing
Instead of three distinct network classes, allow the division between prefix and suffix to occur on arbitrary bit boundaries
Example:
  Network with 9 hosts; only need 4 bits of suffix to encode
  But the smallest class is class C, 254 hosts, so we’ll waste 245 possible IP addresses
  Classless addressing lets have the 4 bits of suffix we need

## Slide 18: Subnets
In general, IP addresses are assigned so that all computers on the same local area network are on the same subnet
It is customary to use the last byte of the IP address to indicate different subnets
  i.e. class C address
But any portion of the IP address can be designated as a subnet by using a subnet mask. IP addresses are binary numbers, so partial bytes can be used as subnets.

## Slide 19: Example Subnet

## Slide 20: Subnet Masks
Typical subnet mask: 255.255.255.0
  First 3 bytes all on the same subnet, only varies in the last byte
  255 = 11111111 in binary. The bits form a “mask” – where there is a 1, this means the subnet is the same.
    192.168.0.1, 192.168.0.2, 192.168.0.55
Subnet mask: 255.255.254.0
  Mask = 11111111 11111111 11111110 00000000
  1.1.1.5 on the same subnet as 1.1.0.5 ?
  00000001 00000001 00000001 00000101 vs
  00000001 00000001 00000000 00000101 YES
  1.1.1.5 on the same subnet as 1.1.2.5 ?
  00000001 00000001 00000001 00000101 vs
  00000001 00000001 00000010 00000101 NO

## Slide 21: Subnets and Subnet Masks
Subnet mask lets us divide the address space on arbitrary bit boundaries
  Good for better allocation of IP addresses
How will computers and routers use the subnet mask?
  A host
    When sending to a destination IP address
    Compare destination IP address to our own subnet mask
    If dest is on the same subnet, just broadcast data on LAN
    If dest on another subnet, send to a gateway or router
Local routers route within subnetted network
  Use subnet mask with the network address of attached networks to determine proper destination

## Slide 22: CIDR Notation
CIDR = Classless Inter-Domain Routing
  Notation for classless addresses
  Specifies the mask associated with an address
  Appends a slash to the address with the size of the mask in decimal
    Examples:
      128.10.0.0/16
        says 16 bit prefix, 16 bit suffix (Class B)
      128.211.0.16/28
        28 bit prefix, 4 bit suffix

## Slide 23: CIDR Example
Why didn’t the lowest start at 0000 and highest at 1111?
One disadvantage; not so easy to read host values from decimal

## Slide 24: Dynamic Addressing
Every computer knows its network layer address from a configuration file. However, each time the computer is moved, or its network is assigned a new address, the software on each individual computer must be updated.
Solution: dynamic addressing. With this approach, a server is designated to supply a network layer address to a computer each time the computer connects to the network from an available “pool” of addresses
  Assigns “Next Available” address
  Simplifies roaming computers, dial-up
Two standards for dynamic addressing are commonly used in TCP/IP networks:
  Bootstrap Protocol (bootp)
  Dynamic Host Control Protocol (DHCP)

## Slide 25: Routers and IP Addresses
IP address depends on network address
What about routers - connected to two networks?
IP address specifies an interface, or network attachment point, not necessarily a computer
  Router has multiple IP addresses - one for each interface

## Slide 26: Multi-Homed Hosts
Hosts (that do not forward packets) can also be connected to multiple networks
  If it forwards packets, it’s a router
Can increase reliability and performance
  If one network fails, the host can still reach the internet through the second connection
  Can also send data on multiple networks for increased performance
Multi-homed hosts also have one address for each interface

## Slide 27: Binding Protocol Addresses
Upper levels of protocol stack use protocol addresses , e.g. IP Address
Network hardware must use hardware address for eventual delivery
Protocol address must be translated into hardware address for delivery; how can this be done?
  This address translation is only necessary for the local LAN.
    Why? Consider if we need the hardware address if sending to a remote computer across the Internet…

## Slide 28: Ethernet ARP: Address Resolution Protocol
Ethernet (MAC) addresses are different than IP addresses. Given an IP address for a machine on the same LAN, what is its MAC address?
  Solution: ARP - Address Resolution Protocol
Each IP node (Host, Router) on the LAN has ARP module and Table. This operates at the Data Link layer
ARP Table: IP/MAC address mappings for some LAN nodes
< IP address; MAC address; TTL>
…
TTL (Time To Live): timer, typically 20 min

## Slide 29: ARP (more)
Host A wants to send packet to destination IP addr XYZ on same LAN
Source Host first checks own ARP Table for IP addr XYZ
If XYZ not in the ARP Table, ARP module broadcasts ARP pkt:
< XYZ, MAC (?) >
ALL nodes on the LAN accept and inspect the ARP packet
Node XYZ responds with unicast ARP pkt carrying own MAC addr:
< XYZ, MAC (XYZ) >
MAC address cached in ARP Table for future use
Host A then sends unicast data packet to MAC(XYZ)
Why not broadcast the data in the first place rather than incur three separate transmissions?

## Slide 30: ARP Table Lookup
Use a simple list containing IP address and hardware address for each host on net
Search on IP address and extract corresponding hardware address
  Note that all IP addresses have same prefix; can save space by dropping prefix

## Slide 31: ARP Table Lookup
Sequential search may be prohibitively expensive (O(n))
Can use indexing or hashing for O(1) lookup
Indexing - use hostid part of IP address as list (array) index
    Hashing - use hashing function on hostid to generate list index

## Slide 32: ARP Message Exchange Example
W ARP’s for Y’s IP Address
Everyone hears the ARP
Only Y responds with a Unicast message (still broadcast on bus)

## Slide 33: ARP Message Contents
Maps protocol address to hardware address
Both protocol address and hardware address sizes are variable
  Ethernet = 6 octets
  IP = 4 octets
Can be used for other protocols and hardware types but in reality just used for Ethernet/IP

## Slide 34: ARP Message Format
HARDWARE ADDRESS TYPE = 1 for Ethernet
PROTOCOL ADDRESS TYPE = 0x0800 for IP
OPERATION = 1 for request, 2 for response
  Contains both target and sender mappings from protocol address to hardware address
  Request sets hardware address of target to 0
  Target can extract hardware address of sender (saving an ARP request)
  Target exchanges sender/target in response

## Slide 35: Sending an ARP Request
Sender constructs ARP message
ARP message carried as data in hardware frame - encapsulation
Uses separate frame type
Ethernet uses type 0x0806

## Slide 36: Routing Packet to another LAN
Say, route packet from source IP addr <111.111.111.111> to destination addr <222.222.222.222>
In routing table at source Host, find router 111.111.111.110
In ARP table at source, find MAC address E6-E9-00-17-BB-4B, etc. ARP does not span LANs!