## Slide 1: Packet-Based Transmission
CS442

## Slide 2: Frames
Packet = Small block of data
  Good for sending data of shared networks, e.g. multiplexed
Frame = Packet, but in the context of a specific type of network
  To send a frame, the sender and receiver must agree on the format of the frame
  i.e. we must know how to specify the beginning and the end of each frame
  Synchronous - block of data transmitted without start or stop bits, requires synchronized clock (or embed clock signal in data, e.g. Manchester encoding)

## Slide 3: Frames - Overview
Need to indicate start and end of block
Use preamble and postamble
  e.g. block of 11111111 patterns ending in 11111110
More efficient (lower overhead) than async for large blocks of data
  Consider a block that requires 8 bytes of overhead (preamble, postamble, other bookkeeping) with 100 information characters, or 800 bits.
  Transmission Efficiency = 800 / 800+64 = 92.6% efficiency
  Using async with start/stop bit, 8 data bits: 800 / 800+200 = 80% efficiency
  Efficiency goes up the larger our blocks are, assuming the overhead bytes stay the same. Why not make our blocks even bigger?

## Slide 4: Transmission Efficiency

## Slide 5: Bit Stuffing with HDLC
Delimit frame at both ends with 01111110
May close one frame and open another
Receiver hunts for flag sequence to synchronize
Bit stuffing used to avoid confusion with data containing 01111110
  If sender wants to send six 1’s as data then it really sends five 1’s and then a 0, followed by a 1: 1111101
  Receiver needs logic to check the next bit after 5 bits are received. If it is 0, then the 0 is deleted and the next bit is read.
  If receiver reads 1 and seventh bit is 0, accept as flag
  Known as the transparency problem

## Slide 6: Byte Stuffing
PPP packet layout
Flag Address Control Message CRC-16 Flag
1 byte 1 byte 1 byte variable 2 bytes 1 byte
SLIP packet layout
End Message End
1 byte variable 1 byte
Uses Escape Character to avoid Transparency Problem
More on the frame field formats later
Same problem at the Byte Level

## Slide 7: Error Detection
Additional bits added by transmitter for error detection code
Parity
  Value of parity bit is such that character has even (even parity) or odd (odd parity) number of ones
  Even number of bit errors goes undetected

## Slide 8: Polynomial Checking
Polynomial checking adds 1 or more characters to the end of the message based on a mathematical algorithm.
With checksum, 1 byte is added to the end of the message. It is obtained by summing the message values,and dividing by 255. The remainder is the checksum. (95% effective)
With CRC (Cyclic Redundancy Check), 8, 16, 24 or 32 bits are added, computed by calculating a remainder to a division problem. (99.969% with 8-bit, 99.99% with 16 bit).
  See book for more details on implementing CRC

## Slide 9: Forward Error Correction
Forward error correction uses codes containing sufficient redundancy to prevent errors by detecting and correcting them at the receiving end without retransmission of the original message.
  Hamming code
  Hagelbarger code (corrects up to 6 consecutive bit errors)
  Bose-Chaudhuri code

## Slide 11: Error Control
Detection and correction of errors
Lost frames
Damaged frames
Automatic Repeat reQuest (ARQ)
  Error detection
  Positive acknowledgment
  Retransmission after timeout
  Negative acknowledgement and retransmission
More on this later

## Slide 12: LAN Technologies
Simplest is point to point
  Computers connected by communication channels that each connect exactly two computers
  Allows flexibility in communication hardware, packet formats, etc.
  Provides security and privacy because communication channel is not shared
But it doesn’t scale

## Slide 13: LAN Technologies
Reduce cost by reducing number of connections via a shared network
But ... attached computers compete for use of shared connection
Local communication almost exclusively LAN
  Works out OK though due to locality of reference
  Principle that we access computers nearby more frequently than those far away
Long distance almost exclusively point-to-point
  SMDS
  ATM
  Modem / PPP

## Slide 14: LAN Topologies

## Slide 15: Bus and Tree Properties
Multipoint medium
Transmission propagates throughout medium
Heard by all stations
  Need to identify target station, each station has unique address
Full duplex connection between station and tap
  Allows for transmission and reception
Need to regulate transmission
  To avoid collisions
  To avoid hogging, data in small blocks - frames

## Slide 16: Frame Transmission - Bus LAN
Data broadcast to all computers
Only one system may transmit at a time or we get a collision
No transmissions if cable is cut
Typically coax cable

## Slide 17: Ring Topology
Repeaters joined by point to point links in closed loop
  Receive data on one link and retransmit on another
  Links unidirectional
  Stations attach to repeaters
Data in frames
  Circulate past all stations
  Destination recognizes address and copies frame
  Frame circulates back to source where it is removed
Media access control determines when station can insert frame

## Slide 18: Frame Transmission Ring LAN

## Slide 19: Star Topology
Each station connected directly to central node
  Usually via two point to point links
Central node can broadcast
  Physical star, logical bus
  Only one station can transmit at a time
Central node can act as frame switch
  Prevents broadcast to other stations except destination, can increase network efficiency
Typically use twisted pair as the medium

## Slide 20: Two Level Star Topology
Can connect hubs to hubs

## Slide 21: Methods for Media Access Control
Needed to keep collisions from happening
Round robin
  Good if many stations have data to transmit over extended period
Reservation
  Good for stream traffic
Contention
  Good for bursty traffic
  All stations contend for time
  Distributed
  Simple to implement
  Efficient under moderate load
  Tend to collapse under heavy load

## Slide 22: Media Access Control - Ethernet (CSMA/CD)
Original form: 10 Mbps, or 1.25 Mbytes/sec
Broadcast bus
Carriers Sense Multiple Access with Collision Detection
  Distributed access control; i. e., no central control on when you can transmit
  Stations randomly access medium, contend for access
  hardware gets every packet
Xerox - Ethernet
IEEE 802.3

## Slide 23: Ethernet’s Predecessor - ALOHA
Packet Radio
When station has frame, it sends
Station listens (for max round trip time) plus small increment
If ACK, fine. If not, retransmit
If no ACK after repeated transmissions, give up
Frame check sequence (as in HDLC)
If frame OK and address matches receiver, send ACK
Frame may be damaged by noise or by another station transmitting at the same time (collision)
Any overlap of frames causes collision
Max utilization 18% - propagation delay < transmission time, high chance of collision! Can wait/listen for free medium first

## Slide 24: CSMA
Propagation time is much less than transmission time
  Travel at about 70% the speed of light
All stations know that a transmission has started almost immediately
Max utilization depends on propagation time (medium length) and frame length
  Longer frame and shorter propagation gives better utilization
First listen for clear medium (carrier sense)
If medium idle, transmit
If two stations start at the same instant, collision
Wait reasonable time (round trip plus ACK contention)
No ACK then retransmit

## Slide 25: If Busy?
If medium is idle, transmit
If busy, listen for idle then transmit immediately
If two stations are waiting, collision

## Slide 26: CSMA/CD
With CSMA, collision occupies medium for duration of transmission
Stations listen whilst transmitting
If medium busy
  listen for idle, then transmit
Else if medium idle
  transmit
  Listen for collision
  If collision detected, jam then cease transmission
    After jam, wait random time then start again
    Binary exponential back off
  Else wait min idle time - give others nodes a chance
    Distributed fairness, 51.2us for 10Mbps

## Slide 27: CSMA/CD Operation
Frames must be long enough to detect collision during transmission!

## Slide 28: Collision Retransmission
Retransmit up to N attempts, e.g. 16
If collision, must send jam signal, random backoff and retransmit
  Jam signal == 512 bits (64 bytes), to ensure the end nodes hear the collision
  The Ethernet minimum frame is 64 bytes (46 data)
Binary exponential algorithm
  Wait 1, 2, 4, 8 … 2m time- slots, etc. where m=Min(10, nth retry)
  Packets can be lost due to collision, especially if network is heavily used
Modern network cards can saturate cable; only ~30% utilization under heavy transmission load

## Slide 29: Collision Detection
On baseband bus, collision produces much higher signal voltage than signal
Collision detected if cable signal greater than single station signal
Signal attenuated over distance
Limit distance to 500m (10Base5) or 200m (10Base2)
For twisted pair (star-topology) activity on more than one port is collision
Special collision presence signal

## Slide 30: Gigabit Ethernet - Differences
Basically, the same as regular Ethernet but faster
Carrier extension
  Frames at least 4096 bit-times long
  Why? Propagation time is too short, and we want the transmission time longer than the propagation time to detect collisions
Frame bursting
  Allows many small frames to be transmitted consecutively up to a limit to avoid carrier extension on short frames

## Slide 31: Gigabit Ethernet - Physical
1000Base-SX
  Short wavelength, multimode fiber
1000Base-LX
  Long wavelength, Multi or single mode fiber
1000Base-CX
  Copper jumpers <25m, shielded twisted pair
1000Base-T
  4 pairs, cat 5 UTP
Signaling - 8B/10B

## Slide 32: Gigabit Ethernet Alliance
http://www.gigabit-ethernet.org
  3Com, Bay Networks, Cisco, Compaq, Granite Systems, Intel, LSI Logic, Packet Engines, Sun Microsystems,UB Networks, VLSI Technology
Selling points
  Relatively low cost?
  Easy migration
  New emphasis on network applications driving growth

## Slide 33: Token Ring (802.5)
MAC protocol
  Small frame (token) circulates when idle
  Station waits for token
  If no data to transmit, forwards token immediately
  If data to transmit, “Holds” token temporarily
  Sends data frame, can send multiple frames up to some maximum number
  Frame(s) make round trip and are absorbed by transmitting station
  Station then inserts new token when transmission has finished and leading edge of returning frame arrives
Under light loads, some inefficiency
Under heavy loads, round robin

## Slide 34: Token Ring Operation
A sends to C
C sends to A and D

## Slide 35: FDDI
Fiber Distributed Data Interface (Can also run over twisted pair at shorter distances)
100Mbps
LAN and MAN applications
Token Ring

## Slide 36: FDDI MAC Protocol
As for 802.5 except:
  Station seizes token by aborting token transmission
  Once token captured, one or more data frames transmitted
  New token released as soon as transmission finished
Two rings for reliability
Allows data frames from multiple senders to be on the ring at once, higher utilization

## Slide 37: FDDI – Multiple Rings
FDDI uses counter-rotating rings in which data flows in opposite directions
In case of fiber or station failure, remaining stations loop back and reroute data through spare ring
All stations automatically configure loop back by monitoring data ring

## Slide 38: FDDI Operation

## Slide 39: LAN Generations
First
  CSMA/CD and token ring
  Terminal to host and client server
  Moderate data rates
Second
  FDDI
  Backbone
  High performance workstations
Third
  ATM / Gigabit Ethernet
  Aggregate throughput and real time support for multimedia applications

## Slide 40: ATM LANs
Asynchronous Transfer Mode
Virtual circuit
Types of ATM LANs
  Gateway to ATM WAN, acts as router
    Need LAN encapsulation (LANE server or edge switch) if carrying ethernet traffic
    Maps ethernet address to Virtual Circuit identifier, broadcast
  Backbone ATM switch
    Single ATM switch or local network of ATM switches
  Workgroup ATM
    End systems connected directly to ATM switch
    Need to replace ethernet cards, ATM operates at data link layer!
  Mixed system

## Slide 41: Example ATM LAN

## Slide 42: ATM LAN HUB

## Slide 43
ATM at Dallas Cowboys (www.dallascowboys.com)
Notes: OC-3 = Optical Carrier, 155Mbps

## Slide 44
ATM inside Reuters News

## Slide 45: ATM Forum
Standards body for ATM
  http://www.atmforum.org
Some members
  AT&T
  Cisco
  3Com
  IBM
  Lucent
  LSI Logic

## Slide 46: Wireless LANs
IEEE 802.11
Basic service set (cell)
  One or more stations using same MAC protocol, together with an access point or base station
  Typically some radius (~200 ft) from the access point
  Competing to access shared medium
  May connect to backbone via access point (bridge)
Extended service set
  Two or more BSS connected by distributed system
  Appears as single logic LAN to Data Link layer

## Slide 47: Wireless LAN - Physical
Infrared
  1Mbps and 2Mbps
  Wavelength 850-950nm
Direct sequence spread spectrum
  2.4GHz ISM band
  Up to 7 channels
  Each 1Mbps or 2Mbps
Frequency hopping spread spectrum
  2.4GHz ISM band
  1Mbps or 2Mbps
Others under development

## Slide 48: 802.11 Media Access Control
Instead of CSMA/CD, uses CSMA/CA
  Carrier Sense Multiple Access, Collision Avoidance
No collision detection, aims at avoiding collisions in the first place
Even with collision detection, if no collision is sensed one could still occur at the receiver
A, C send to B but no direct signal between A-C

## Slide 49: 802.11 Media Access
If media is idle for time DIFS (Distributed Inter Frame Space) then allowed to transmit
If media is busy
  Wait until media is free for time DIFS
  Then wait an ADDITIONAL random backoff time before sending instead of immediately as in 802.3
Receiver might get a collision, but no detection for one – instead the CRC will (hopefully) fail
  Send an ACK back if data correctly received
  Needs to send ACK due to lack of collision detection
  If sender doesn’t receive ACK in time period, resends

## Slide 50: 802.11 Media Access
Also supports a way to reserve channel access, avoids hidden station problem
Sender sends short Request To Send (RTS)
Receiver sends short Clear To Send (CTS) with permission to the Sender
  All other stations also hear the CTS, and have to withhold sending until transmission is complete
Sender sends data
Recipient sends ACK if successful
  Other stations also hear the ACK, can now issue their own RTS
Might have collisions with RTS or CTS but not with Data or ACK. If collisions, stations requesting to send will not get a CTS and will have to wait random time to re-submit the RTS

## Slide 51: Frame Identification
Previous section on LAN technology described techniques for providing connectivity between computers
Need to devise technique for delivering message through LAN medium to single, specific destination computer
Sending computer uses a hardware address to identify the intended destination of a frame
Sending computer also identifies type of data carried in the frame

## Slide 52: Specifying a Destination
Data sent across a shared network reaches all attached stations - for all LAN topologies
  Not the switched technology though!
Interface hardware detects delivery of frame and extracts frame from medium
But ... most applications want data to be delivered to one specific application on another computer - not all computers

## Slide 53: Hardware Addressing
Most network technologies have a hardware addressing scheme that identifies stations on the network
Each station is assigned a numeric hardware address or physical address
Sender includes hardware address in each transmitted frame
Only station identified in frame receives copy of frame
Most LAN technologies include sender's hardware address in frame, too

## Slide 54: LAN Hardware and Packet Filtering
A little detail about organization of LAN hardware and computer:

## Slide 55: LAN Hardware and Packet Filtering
LAN interface handles all details of frame transmission and reception
  Adds hardware addresses, error detection codes, etc. to outgoing frames
  May use DMA to copy frame data directly from main memory
  Obeys access rules (e.g., CSMA/CD) when transmitting
  Checks error detection codes on incoming frames
  May use DMA to copy data directly into main memory
  Checks destination address on incoming frames
If destination address on incoming frame matches the local station's address, a copy of the frame is passed to the attached computer
Frames not addressed to the local computer are ignored and don't affect the local computer in any way

## Slide 56: Broadcasting
Some applications want to broadcast messages to all stations on the LAN
Shared communication channel can make broadcast efficient - message is delivered to all stations
Special broadcast address used to identify broadcast messages, which are captured by all stations
  Station passes data up if the address on the message matches its own address or the broadcast address

## Slide 57: Multicast
What if some computers on a LAN want to broadcast for their app, but others don’t?
  Those that don’t are stuck processing a bunch of broadcast data they don’t care about
  Broadcast data is not filtered, it is passed up the networking layer stack
  Solution is multicasting
Set up a multicast address
  This address passes to the network interface
  Interface can then choose to pass data up if the frame’s address matches the station’s address or broadcast address or multicast address

## Slide 58: Ethernet Addressing
Each NIC has a unique MAC address, assigned by IEEE in its ROM
48-bit integer, 6 unsigned char bytes
  Broadcast address: FF FF FF FF FF FF
  Multicast address: 01 XX XX XX XX XX
  unicast address the rest, e.g.: 00 02 B3 9F 3A 1B
  first 3 bytes are manufacturer code
  Intel: 00 02 B3
  Sun: 08 00 20
  3Com Europe: 00 50 99
See http://standards.ieee.org/db/oui/ for more

## Slide 59: Ethernet Frame Formats
Two formats!
  Ethernet 2.0 (Xerox, Unix)
  IEEE 802.3 (Novell / ISO / Unix)
    Has the two sub-layers for LLC (logical link control) and MAC

## Slide 60: Ethernet Frame Formats
Destination Source Length LLC Type Message CRC-32
address address 2 bytes 6 bytes 2 bytes variable 4 bytes
6 bytes 6 bytes 38-1492 bytes
IEEE 802.3, Min length=64, Max=1518 bytes
Ethernet 2 Format - Min length=64, Max=1518 bytes
Destination Source Type Message CRC-32
address address 2 bytes variable 4 bytes
6 bytes 6 bytes 46-1500 bytes
Type indicates higher level protocol or control:
IP = 0x0800, AppleTalk over Eth: 0x809B ARP = 0x0806, RARP=0x8035

## Slide 61: Ethernet Frame Formats
How can an ethernet driver tell the difference between the two frame types in a heterogenous network?
The frame formats don’t overlap (at least not for most types)
  802.3 Len >= 46 && <= 1500
  Ethernet IP Type == 0x800, 2048 in decimal

## Slide 62: Other Things to Note
Ethernet 2 format didn’t specify the length of the frame
  How do we know how large the frame is?
  Recipient has to read in all the data and then compute that the last 4 bytes are CRC, stuff in between Type and CRC is the payload
In 802.3 a portion of the LLC and Length fields are called SNAP (SubNetwork Attachment Point)

## Slide 63: MTU – Maximum Transmission Unit
We said that Ethernet has a maximum frame size of 1518 bytes (less for the data, depending on Ethernet 2 vs. 802.3)
Limit on size of frame transmitted at data link layer
To see MTU on UNIX:
  netstat -in
  Ethernet 2: 1500
802.3: 1492
Microsoft’s PPP: 1500 (576 better for high-latency modems)
If the Network Layer has a bigger packet than MTU, it must be fragmented

## Slide 64: Ethernet Headers and Trailers
Both formats have an 8 byte preamble used for synchronization (alternating 1’s and 0’s, makes a regular square wave)
CRC code:
  If computed CRC <> packet’s CRC, the packet is thrown away
  Rely on higher level protocols for data integrity
No retries, ACKs, or NAKs, so-called “best effort”
  Ethernet is an unreliable protocol
  Makes it easy and cheap though!
  what does/doesn’t ethernet CRC guarantee you?

## Slide 65: Ethernet Packets
Does CRC catch all bit errors?
No!
Are most errors caught?
Yes!
Can you guarantee your packet will arrive?
No! Collision, congestion, Noise
If going through 10 routers or bridges, can you guarantee reliability?
Definitely no!

## Slide 66: Network Analyzer
A network analyzer or network monitor or ``network sniffer'' is used to examine the performance of or debug a network
Can report statistics such as capacity utilization, distribution of frame size, collision rate or token circulation time
Can record and display specific frames, to understand and debug packet transmissions and exchanges

## Slide 67: Network Analyzer
Basic idea is a computer with a network interface that receives all frames
Sometimes called promiscuous mode
Many desktop computers have interface that can be configured for promiscuous mode
  Combined with software, computer can examine any frame on LAN
  Communication across a LAN is not guaranteed to be private!
Computer receives and displays (but does not respond to) frames on the LAN
We’ll have a homework assignment later using a network analyzer