## Slide 1: Transport Layer: TCP/UDP
Chapter 24, 16

## Slide 2: Transport Layer
Purpose of transport layer services:
  multiplexing/demultiplexing
  reliable data transfer
  flow control
  congestion control
Connection-less transport: UDP
Connection-oriented transport: TCP
  reliable transfer
  flow control
  connection management

## Slide 3: Transport services and protocols
provide logical communication between application processes running on different hosts
transport protocols run in end systems via software
transport vs network layer services:
network layer: data transfer between end systems
transport layer: data transfer between processes
  relies on, enhances, network layer services
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 4: Transport-layer protocols
Internet transport services:
reliable, in-order unicast delivery (TCP)
  congestion
  flow control
  connection setup
unreliable (“best-effort”), unordered unicast or multicast delivery: UDP
services not available:
  real-time
  bandwidth guarantees
  reliable multicast
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 5: Multiplexing/demultiplexing
application
transport
network
M
P2
application
transport
network
Recall: segment - unit of data exchanged between transport layer entities
  aka TPDU: transport protocol data unit or “packet”
receiver
H
t
H
n
Demultiplexing: delivering
received segments to
correct app layer processes
segment
segment
M
application
transport
network
P1
M
M
M
P3
P4
segment
header
application-layer
data

## Slide 6: Multiplexing/demultiplexing
multiplexing/demultiplexing:
based on sender, receiver port numbers, IP addresses
  source, dest port #s in each segment
  recall: well-known port numbers for specific applications
gathering data from multiple
app processes, enveloping
data with header (later used
for demultiplexing)
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format
Multiplexing:

## Slide 7: Multiplexing/demultiplexing: examples
host A
server B
source port: x
dest. port: 23
source port:23
dest. port: x
port use: simple telnet app
Web client
host A
Web
server B
Web client
host C
Source IP: C
Dest IP: B
source port: x
dest. port: 80
Source IP: C
Dest IP: B
source port: y
dest. port: 80
port use: Web server
Source IP: A
Dest IP: B
source port: x
dest. port: 80

## Slide 8: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out of order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
Why is there a UDP?
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small segment header
no congestion control: UDP can blast away as fast as desired

## Slide 9: UDP: more
often used for streaming multimedia apps
  Controversial: no congestion control
other UDP uses (why?):
  DNS
  SNMP
reliable transfer over UDP: add reliability at application layer
  application-specific error recover!
source port #
dest port #
32 bits
Application
data
(message)
UDP segment format
length
checksum
Length, in
bytes of UDP
segment,
including
header

## Slide 10: UDP checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
    Toss data OR
    Pass to app with warning
  YES - no error detected.
Goal: detect “errors” (e.g., flipped bits) in transmitted segment

## Slide 11: Connection Oriented Transport Protocol Mechanisms
Properties of connection-oriented Transport Protocols:
  Logical connection
  Establishment
  Maintenance termination
  Reliable
  e.g. TCP

## Slide 12: Connection-Oriented Transport via Reliable Network Layer
Transport Layer Services like TCP are complicated – to start, let’s first assume we are working with a reliable network layer service
  e.g. reliable packet switched network using X.25
  e.g. frame relay using LAPF control protocol
  e.g. IEEE 802.3 using connection oriented LLC service
  NOT IP! IP is unreliable
Assume arbitrary length message
Transport service is end to end protocol between two systems on same network

## Slide 13: Issues in a Simple Transprot Protocol
If we have a reliable network layer, then the transport layer must consider:
  Addressing
  Multiplexing
  Flow Control
  Connection establishment and termination

## Slide 14: Addressing
Target user specified by:
  User identification
    Usually host, port
      Called a socket in TCP/UDP
    Port represents a particular transport service (TS), e.g. HTTPD
  Transport protocol identification
    Generally only one per host
    If more than one, then usually one of each type
      Specify transport protocol (TCP, UDP)
  Host address
    An attached network device
    In an internet, a global internet address (IP Address)
    A well-known address or lookup via name server

## Slide 15: Multiplexing
Multiple users employ same transport protocol
User identified by port number or service access point (SAP)
Described previously

## Slide 16: Flow Control
Can be difficult than flow control at the data link layer – data is likely traveling across many networks, not one network. Some potential problems:
  Longer transmission delay between transport entities compared with actual transmission time
    Delay in communication of flow control info
  Variable transmission delay
    Difficult to use timeouts
Flow may be controlled because:
  The receiving user cannot keep up
  The receiving transport entity cannot keep up
  If either happens, the results is a buffer that can get full and eventually lose data

## Slide 17: Model of Frame Transmission
Diagram for Frame/Packet Transmission
We’ll use this model to discuss flow control issues

## Slide 18: Coping with Flow Control Requirements (1)
Do nothing
  Segments that overflow are discarded
  Sending transport entity will fail to get ACK and will retransmit
    Thus further adding to incoming data and could exacerbate the flow control problem
Refuse further segments from network layer
  Clumsy
  Multiplexed connections are controlled on aggregate flow

## Slide 19: Coping with Flow Control Requirements (2)
One protocol: Stop-and-Wait
  Sender must wait for recipient to send ACK before sending the next packet
    Not very efficient usage of the network, only one outstanding message can be in transit at a time
  Works well on reliable network
    Failure to receive ACK is taken as flow control indication
  Does not work well on unreliable network
    Cannot distinguish between lost segment and flow control

## Slide 20: Coping with Flow Control
Credit-Based Scheme
  Credit = How much data sender can transmit
    Sliding window idea, sender can send a number of frames up to the window size
    Receiver sends single ACK that acknowledges all previous frames
    Window size varies based on credit available
    Receiver can control credit of the sender
      In acknowledgement, receiver could change the window size
  Advantages
    Better network usage, allows outstanding messages to be in transit than Stop-And-Wait
    More effective on unreliable network
      Decouples flow control from ACK
    May ACK without granting credit and vice versa
  Each octet has sequence number
  Each transport segment has a sequence number, acknowledgement number and window size in header

## Slide 21: Sliding Window Enhancements
Receiver can acknowledge frames without permitting further transmission (Receive Not Ready)
Must send a normal acknowledge to resume
If full duplex two-way communications, we need two windows: one for transmit and one for receive
  Piggybacking – if sending data and acknowledgement frame, combine together
More efficient than stop-and-wait since many frames may be in the pipeline

## Slide 22: Example Sliding Window
RR N=Receive Ready on N
Fixed Window Size

## Slide 23: Use of Header Fields
For credit-based window size
  When sending, Sequence Number is that of first octet in segment
  ACK includes AN=i (Acknowledgement Number), W=j (Window Size)
  All octets through SN=i-1 acknowledged
    Next expected octet is i
  Permission to send additional window of W=j octets
    i.e. octets through i+j-1

## Slide 24: Credit Allocation Example
200 octets per segment
A, B initially “synched”

## Slide 25: Establishment and Termination
Even with a reliable network service, both ends need to “set up” the connection:
  Allow each end to know the other exists and is listening
  Negotiation of optional parameters
    Maximum Segment Size
    Maximum Window Size
  Triggers allocation of transport entity resources
    Buffer space allocated
    Entry in connection tables

## Slide 26: Connection State Diagram – Reliable Network Service
Start State
SYN=Sync
FIN=Finish

## Slide 27: Connection Establishment

## Slide 28: Setting up the connection
What if a SYN received while not in the Listen state?
  Reject with RST (Reset)
  Queue request until matching open issued
  Signal TS user to notify of pending request

## Slide 29: Termination
Connection can be terminated by sending FIN
Graceful termination
  CLOSE_WAIT state and FIN_WAIT must accept incoming data until FIN received
  Ensures both sides have received all outstanding data and that both sides agree to connection termination before actual termination

## Slide 30: Unreliable Network Service
Now let’s look at the more general case if we are building our transport service on top of an unreliable network layer
An unreliable network service makes the transport layer much more complicated if we want to ensure reliability
Examples of unreliable network services:
  Internet using IP,
  Frame Relay using LAPF
  IEEE 802.3 using unacknowledged connectionless LLC
Segments may get lost
Segments may arrive out of order

## Slide 31: Problems
Ordered Delivery
Retransmission strategy
Duplication detection
Flow control
Connection establishment
Connection termination
Crash recovery

## Slide 32: Ordered Delivery
Segments may arrive out of order
Number segments sequentially
TCP numbers each octet sequentially
Segments are numbered by the first octet number in the segment
TCP actually numbers segments starting at a random value!
  Minimizes possibility that a segment still in the network from an earlier, terminated connection between the same hosts is mistaken for a valid segment in a later connection (who would also have to happen to use the same port numbers)

## Slide 33: Retransmission Strategy
Need to re-transmit when
  Segment damaged in transit
  Segment fails to arrive
Receiver must acknowledge successful receipt
Use cumulative acknowledgement
Time out waiting for ACK triggers re-transmission
How long to wait until re-transmitting?
  Too short: duplicate data
  Too long: Unnecessary delay delivering data

## Slide 34: Timer Value
Fixed timer
  Based on understanding of network behavior
  Can not adapt to changing network conditions
  Too small leads to unnecessary re-transmissions
  Too large and response to lost segments is slow
  Should be a bit longer than Round Trip Time (RTT)
Adaptive scheme
  E.g. set timer to average of previous ACKs
  Problems:
    Sender may not ACK immediately
    Cannot distinguish between ACK of original segment and re-transmitted segment
    Conditions may change suddenly

## Slide 35: Duplication Detection
If ACK lost, segment is re-transmitted
Receiver must recognize duplicates
Duplicate received prior to closing connection
  Receiver assumes ACK lost and ACKs duplicate
  Sender must not get confused with multiple ACKs
  Sequence number space large enough to not cycle within maximum life of segment
Also possible to receive a duplicate after closing the connection!

## Slide 36: Incorrect Duplicate Detection
Illustrates need for the sequence number space to be larger than the maximum possible segment lifetime
Note: cycle back to SN=1

## Slide 37: Flow Control
Can use credit allocation described earlier
Generally little harm if a single ACK/Credit segment is lost, will resynchronize the next time
Problem if B sends AN=i, W=0 closing window
Later, B sends AN=i, W=j to reopen, but this is lost
Sender thinks window is closed, receiver thinks it is open
Solution: use window timer
If timer expires, send something to break the deadlock
  Could be re-transmission of previous segment

## Slide 38: Connection Establishment
Two way handshake
  A send SYN, B replies with SYN
  Lost SYN handled by re-transmission
    Can lead to duplicate SYNs
  Ignore duplicate SYNs once connected
Lost or delayed data segments can cause connection problems
  Segment from old connections

## Slide 39: Two Way Handshake: Obsolete Data Segment

## Slide 40: Two Way Handshake: Obsolete SYN Segment
B expects SN j
A wants new connection, picks SN k

## Slide 41: Connection Establishment – Three Way Handshake
Solution: Explicitly acknowledge each other’s SYN and sequence number
  Use SYN i
  Need ACK to include i
Called the Three Way Handshake

## Slide 42: Three Way Handshake: Examples

## Slide 43: Three Way Handshake: State Diagram

## Slide 44: Connection Termination
Same problems we had with connection establishment can also occur with connection termination
  Lost or obsolete FIN segment
  Can lose last data segment if FIN arrives before last data segment
Solution: associate sequence number with FIN
Receiver waits for all segments before FIN sequence number
Must explicitly ACK FIN

## Slide 45: Graceful Close
Send FIN i and receive AN i
Receive FIN j and send AN j
Wait twice maximum expected segment lifetime

## Slide 46: Crash Recovery
If the transport service crashes and restarts, after restart all state info is lost
Connection is half open
  Side that did not crash still thinks it is connected
Close connection using persistence timer
  Wait for ACK for (time out) * (number of retries)
  When expired, close connection and inform user
Send RST i in response to any i segment arriving
User must decide whether to reconnect
  Problems with lost or duplicate data

## Slide 47: TCP:Overview RFCs: 793, 1122, 1323, 2018, 2581
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) init’s sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte stream:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers

## Slide 48: TCP Properties
stream orientation. stream of OCTETS (bytes) passed between send/ recv
byte stream is full duplex
  think of it as two independent streams joined with a piggybacking mechanism
  piggybacking - one data stream has control info for the other data stream (going the other way)
unstructured stream
  TCP doesn’t show packet boundaries to applications
  But you can still structure your message if you want
  Recall usage with sockets:
    One write() call to send data
    May require multiple read() calls

## Slide 49: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
rcvr window size
ptr urgent data
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 50: TCP Fields
Source, Destination Port: 16 bits each
Sequence Number: 32 bits
  Sequence # of first data octet in the segment, initialized randomly as described earlier
ACK Number: 32 bits
  Piggybacked ACK, contains sequence number of the next data octet the receiver expects
Header Len: 4 bits
  Number of 32 bit words in the header
Not Used: 6 bits for future use

## Slide 51: TCP Fields
Flags – 6 bits
  URG – Urgent Pointer field significant
  ACK – Ack field significant
  PSH – Push (flush or “push” buffer now, send data to app)
  RST – Reset connection
  SYN – Synchronize sequence numbers
  FIN – No more data
Window – 16 bits
  Flow control credit allocation
Checksum – 16 bits
  One’s complement sum as in UDP
Urgent Pointer – 16 bits
  Last octet in a seq of “urgent” data. Sometimes not interpreted. Urgent data should be processed now, even before any data sitting in the buffer (e.g. send control-c to terminate)
Options – Variable
  Support for timestamping, negotiating MSS

## Slide 52: TCP seq. #’s and ACKs
Seq. #’s:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK
Q: How does the receiver handles out-of-order segments?
  A: TCP spec doesn’t say, - up to implementer
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
time
simple telnet scenario
Note piggybacking!

## Slide 53: TCP: retransmission scenarios
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
time
lost ACK scenario
Host B
X
Seq=92, 8 bytes data
ACK=100
Host A
Seq=100, 20 bytes data
ACK=100
Seq=92 timeout
time
premature timeout,
cumulative ACKs
Host B
Seq=92, 8 bytes data
ACK=120
Seq=92, 8 bytes data
Seq=100 timeout
ACK=120
Sender must be smart enough to ignore duplicate ACK

## Slide 54: TCP Flow Control
receiver: explicitly informs sender of (dynamically changing) amount of free buffer space
  RcvWindow field in TCP segment
sender: keeps the amount of transmitted, unACKed data less than most recently received RcvWindow
sender won’t overrun
receiver’s buffers by
transmitting too much,
too fast
flow control
receiver buffering
RcvBuffer = size or TCP Receive Buffer
RcvWindow = amount of spare room in Buffer

## Slide 55: TCP Round Trip Time and Timeout
Q: how to set TCP timeout value?
longer than RTT
  note: RTT will vary
too short: premature timeout
  unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
  ignore retransmissions, cumulatively ACKed segments
SampleRTT will vary, want estimated RTT “smoother”
  use several recent measurements, not just current SampleRTT

## Slide 56: TCP Round Trip Time and Timeout
EstimatedRTT = (1-x)*EstimatedRTT + x*SampleRTT
Exponential weighted moving average
influence of given sample decreases exponentially fast
typical value of x: 0.1
Setting the timeout
EstimatedRTT plus “safety margin”
large variation in EstimatedRTT -> larger safety margin
Timeout = EstimatedRTT + 4*Deviation

## Slide 57: TCP Connection Management
Three way handshake:
Step 1: client end system sends TCP SYN control segment to server
  specifies initial seq #
Step 2: server end system receives SYN, replies with SYNACK control segment
  ACKs received SYN
  allocates buffers
  specifies server-> receiver initial seq. #

## Slide 58: TCP Connection Management (cont.)
Closing a connection:
Step 1: client end system sends TCP FIN control segment to server
Step 2: server receives FIN, replies with ACK. Closes connection, sends FIN.
Step 3: client receives FIN, replies with ACK.
  Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
client
FIN
server
ACK
ACK
FIN
close
close
closed
timed wait

## Slide 59: Principles of Congestion Control
Congestion:
informally: “too many sources sending too much data too fast for network to handle”
different from flow control!
manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)
A top-10 problem!

## Slide 60: Causes/costs of congestion: scenario 1
two senders, two receivers
one router, infinite buffers
no retransmission
large delays when congested
maximum achievable throughput

## Slide 61: Causes/costs of congestion: scenario 2
one router, finite buffers
sender retransmission of lost packet
“offered load”

## Slide 62: Causes/costs of congestion: scenario 2
if: (goodput)
retransmission only when loss:
Even worse: retransmission of delayed (not lost) packet makes larger than the previous case for the same

in

in’
=

in

out
>
“costs” of congestion:
more work (retrans) for given “goodput”
unneeded retransmissions: link carries multiple copies of pkt

in

out

## Slide 63: Causes/costs of congestion: scenario 3
four senders
multihop paths
timeout/retransmit

in
Q: what happens as and increase ?

in

## Slide 64: Causes/costs of congestion: scenario 3
Another “cost” of congestion:
when packet dropped, any “upstream transmission capacity used for that packet was wasted!
Throughput goes to 0 as the heavy traffic approaches infinity
In everyone’s best interest to “back off” on transmission

## Slide 65: Approaches towards congestion control
End-end congestion control:
no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP
Network-assisted congestion control:
routers provide feedback to end systems
  single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  explicit rate sender should send at
Two broad approaches towards congestion control:

## Slide 66: TCP Congestion Control
end-end control (no network assistance)
transmission rate limited by congestion window size, Congwin, over segments:
w segments, each with MSS bytes sent in one RTT:
throughput =
w * MSS
RTT
Bytes/sec
Congwin

## Slide 67: TCP congestion control:
two “phases”
  slow start
  congestion avoidance
important variables:
  Congwin
  threshold: defines threshold between two slow start phase, congestion control phase
“probing” for usable bandwidth:
  ideally: transmit as fast as possible (Congwin as large as possible) without loss
  Reality:
  increase Congwin until loss (congestion)
  loss: decrease Congwin, then begin probing (increasing) again

## Slide 68: TCP Slowstart
exponential increase (per RTT) in window size (not so slow!)
loss event: timeout (Tahoe TCP) and/or or three duplicate ACKs (Reno TCP)
(What causes duplicate ACKs?)
initialize: Congwin = 1
for (each segment ACKed)
Congwin++
until (loss event OR
CongWin > threshold)
Slowstart algorithm
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 69: TCP Congestion Avoidance
/* slowstart is over */
/* Congwin > threshold */
Until (loss event) {
every w segments ACKed:
Congwin++
}
threshold = Congwin/2
Congwin = 1
perform slowstart
Congestion avoidance
1

## Slide 70: TCP Fairness
Fairness goal: if N TCP sessions share same bottleneck link, each should get 1/N of link capacity
TCP congestion avoidance:
AIMD: additive increase, multiplicative decrease
  increase window by 1 per RTT
  decrease window by factor of 2 on loss event
AIMD
TCP connection 1
bottleneck
router
capacity C
TCP
connection 2

## Slide 71: Why is TCP fair?
Two competing sessions:
Additive increase gives slope of 1, as throughput increases
multiplicative decrease decreases throughput proportionally
C
C
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
Eventually the two connections fluctuate along equal bandwidth line

## Slide 72: TCP vs. UDP
When to use TCP
  Need reliable network service
  Want flow, congestion control
When to use UDP
  Don’t want overhead of TCP
  Don’t want congestion control! I.e. we don’t want to be “fair”
    Multimedia apps
    Don’t want data rate throttled, but ironically this can lead to unfair transmission rate and could actually bring all traffic to a halt
    Could also be unfair using TCP by opening multiple parallel connections (often done with web data)