## Slide 1: Intro to GPU’s for Parallel Computing

## Slide 2: Goals for Rest of Course
Learn how to program massively parallel processors and achieve
  high performance
  functionality and maintainability
  scalability across future generations
Acquire technical knowledge required to achieve the above goals
  principles and patterns of parallel programming
  processor architecture features and constraints
  programming API, tools and techniques
Overview of architecture first, then introduce architecture as we go

## Slide 3: Equipment
Your own, if CUDA-enabled; will use CUDA SDK in C
  Compute Unified Device Architecture
  NVIDIA G80 or newer
  G80 emulator won’t quite work
Lab machine – uaa-csetesla.duckdns.org
  Ubuntu
  two Intel Xeon E5-2609 @2.4Ghz, each four cores
  128 Gb memory
  Two nVidia Quadro 4000’s
    256 CUDA Cores
    1 Ghz Clock
    2 Gb memory

## Slide 4: Why Massively Parallel Processors
A quiet revolution and potential build-up
  2006 Calculation: 367 GFLOPS vs. 32 GFLOPS
  G80 Memory Bandwidth: 86.4 GB/s vs. 8.4 GB/s
  Until recently, programmed through graphics API
  GPU in every PC and workstation – massive volume and potential impact
Notes: CPU driven by sequential code performance; extracting ILP, branch prediction, ROB, out of order execution, etc.
Graphics focused on pixel-based processing, parallelism - now on every workstation, no longer just supercomputer
Size a factor for many fields, e.g. medical MRI; supercomputer in a workstation sized package

## Slide 5: CPUs and GPUs have fundamentally different design philosophies
DRAM
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU
GPU

## Slide 6: Architecture of a CUDA-capable GPU
Load/store
Global Memory
Thread Execution Manager
Input Assembler
Host
Texture
Texture
Texture
Texture
Texture
Texture
Texture
Texture
Texture
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Load/store
Load/store
Load/store
Load/store
Load/store
Streaming
Processor
(SP)
Streaming
Multiprocessor
(SM)
Building
Block
32 SM’s each with 8 SP’s on one Quadro 4000
Notes: Joint CPU/GPU operation
Each SP can process a FP multiply and a FP multiply/add

## Slide 7: GT200 Characteristics
1 TFLOPS peak performance (25-50 times of current high-end microprocessors)
265 GFLOPS sustained for apps such as Visual Molecular Dynamics (VMD)
Massively parallel, 128 cores, 90W
Massively threaded, sustains 1000s of threads per app
30-100 times speedup over high-end microprocessors on scientific and media applications: medical imaging, molecular dynamics
“I think they're right on the money, but the huge performance differential (currently 3 GPUs ~= 300 SGI Altix Itanium2s) will invite close scrutiny so I have to be careful what I say publically until I triple check those numbers.”
-John Stone, VMD group, Physics UIUC

## Slide 8: Future Apps Reflect a Concurrent World
Exciting applications in future mass computing market have been traditionally considered “supercomputing applications”
  Molecular dynamics simulation, Video and audio coding and manipulation, 3D imaging and visualization, Consumer game physics, and virtual reality products
  These “Super-apps” represent and model physical, concurrent world
Various granularities of parallelism exist, but…
  programming model must not hinder parallel implementation
  data delivery needs careful management
Notes: Do not go over all of the different applications. Let them read them instead.

## Slide 9: Sample of Previous GPU Projects
Application | Description | Source | Kernel | % time
H.264 | SPEC ‘06 version, change in guess vector | 34,811 | 194 | 35%
LBM | SPEC ‘06 version, change to single precision and print fewer reports | 1,481 | 285 | >99%
RC5-72 | Distributed.net RC5-72 challenge client code | 1,979 | 218 | >99%
FEM | Finite element modeling, simulation of 3D graded materials | 1,874 | 146 | 99%
RPES | Rye Polynomial Equation Solver, quantum chem, 2-electron repulsion | 1,104 | 281 | 99%
PNS | Petri Net simulation of a distributed system | 322 | 160 | >99%
SAXPY | Single-precision implementation of saxpy, used in Linpack’s Gaussian elim. routine | 952 | 31 | >99%
TRACF | Two Point Angular Correlation Function | 536 | 98 | 96%
FDTD | Finite-Difference Time Domain analysis of 2D electromagnetic wave propagation | 1,365 | 93 | 16%
MRI-Q | Computing a matrix Q, a scanner’s configuration in MRI reconstruction | 490 | 33 | >99%
Notes: LBM: Fluid simulation
About 20 versions were tried for each app.
Amdahl’s Law

## Slide 10: Speedup of Applications
GeForce 8800 GTX vs. 2.2GHz Opteron 248
10 speedup in a kernel is typical, as long as the kernel can occupy enough parallel threads
25 to 400 speedup if the function’s data requirements and control flow suit the GPU and the application is optimized
Notes: All kernels have large numbers of simultaneously executing threads
Most of the 10X kernels saturate memory bandwidth
Can get better quality as well as being faster; e.g. solve instead of approximate

## Slide 11: GPU History CUDA

## Slide 12: Graphics Pipeline Elements
A scene description: vertices, triangles, colors, lighting
Transformations that map the scene to a camera viewpoint
“Effects”: texturing, shadow mapping, lighting calculations
Rasterizing: converting geometry into pixels
Pixel processing: depth tests, stencil tests, and other per-pixel operations.

## Slide 13: A Fixed Function GPU Pipeline
Host
Vertex Control
Vertex
Cache
VS/T&L
Triangle Setup
Raster
Shader
ROP
FBI
Texture
Cache
Frame
Buffer
Memory
CPU
GPU
Host Interface
Notes: Shifting boundary as GPU power increases; first 3DFX Voodoo card started at Raster Ops; later VS/T&L; faster interface (AGP from PCI); then programmable starting around 2002. Functions in the pipeline stages vary with rendering algorithm

## Slide 14: Texture Mapping Example
Texture mapping example: painting a world map texture image onto a globe object.
Notes: Data independence of pixels provides an opportunity for parallelism

## Slide 15: Anti-Aliasing Example
Triangle Geometry
Aliased
Anti-Aliased

## Slide 16: Programmable Vertex and Pixel Processors
3D Application or Game
3D API: OpenGL or Direct3D
Programmable Vertex Processor
Primitive Assembly
Rasterization & Interpolation
3D API Commands
Transformed Vertices
Assembled Polygons, Lines, and Points
GPU Command & Data Stream
Programmable Fragment Processor
Rasterized Pre-transformed Fragments
Transformed Fragments
Raster Ops
Framebuffer
Pixel Updates
GPU Front End
Pre-transformed Vertices
Vertex Index Stream
Pixel Location Stream
CPU – GPU Boundary
CPU
GPU
An example of separate vertex processor and fragment processor in a programmable graphics pipeline

## Slide 17: GeForce 8800 GPU
2006 – Mapped the separate programmable graphics stages to an array of unified processors
  Logical graphics pipeline visits processors three times with fixed-function graphics logic between visits
  Load balancing possible; different rendering algorithms present different loads among the programmable stages
    Dynamically allocated from unified processors
Functionality of vertex and pixel shaders identical to the programmer
  geometry shader to process all vertices of a primitive instead of vertices in isolation

## Slide 18: Unified Graphics Pipeline GeForce 8800
L2
FB
SP
SP
L1
TF
Thread Processor
Vtx Thread Issue
Setup / Rstr / ZCull
Geom Thread Issue
Pixel Thread Issue
Data Assembler
Host
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
SP
SP
L1
TF
L2
FB
L2
FB
L2
FB
L2
FB
L2
FB
Notes: Graphics problem turns into firing off thousands of threads

## Slide 19: What is (Historical) GPGPU ?
General Purpose computation using GPU and graphics API in applications other than 3D graphics
  GPU accelerates critical path of application
Data parallel algorithms leverage GPU attributes
  Large data arrays, streaming throughput
  Fine-grain SIMD parallelism
  Low-latency floating point (FP) computation
Applications – see http://gpgpu.org
  Game effects (FX) physics, image processing
  Physical modeling, computational engineering, matrix algebra, convolution, correlation, sorting

## Slide 20: Previous GPGPU Constraints
Dealing with graphics API
  Working with the corner cases of the graphics API
Addressing modes
  Limited texture size/dimension
Shader capabilities
  Limited outputs
Instruction sets
  Lack of Integer & bit ops
Communication limited
  Between pixels
  Scatter a[i] = p
Input Registers
Fragment Program
Output Registers
Constants
Texture
Temp Registers
per thread
per Shader
per Context
FB Memory
Notes: Around DirectX9; programmer cast computation into native graphics operations; e.g. take physics problem and map it into a graphics processing rendering problem. Shader paints color onto a pixel; all it does, if you have a shader everything looks like a pixel

## Slide 21: Tesla GPU
NVIDIA developed a more general purpose GPU
Can programming it like a regular processor
Must explicitly declare the data parallel parts of the workload
  Shader processors  fully programming processors with instruction memory, cache, sequencing logic
  Memory load/store instructions with random byte addressing capability
  Parallel programming model primitives; threads, barrier synchronization, atomic operations

## Slide 22: CUDA
“Compute Unified Device Architecture”
General purpose programming model
  User kicks off batches of threads on the GPU
  GPU = dedicated super-threaded, massively data parallel co-processor
Targeted software stack
  Compute oriented drivers, language, and tools
Driver for loading computation programs into GPU
  Standalone Driver - Optimized for computation
  Interface designed for compute – graphics-free API
  Data sharing with OpenGL buffer objects
  Guaranteed maximum download & readback speeds
  Explicit GPU memory management

## Slide 23: Parallel Computing on a GPU
8-series GPUs deliver 25 to 200+ GFLOPS on compiled parallel C applications
  Available in laptops, desktops, and clusters
GPU parallelism is doubling every year
Programming model scales transparently
Programmable in C with CUDA tools
Multithreaded SPMD model uses application data parallelism and thread parallelism
GeForce 8800
Tesla S870
Tesla D870

## Slide 24: Overview
CUDA programming model – basic concepts and data types
CUDA application programming interface - basic
Simple examples to illustrate basic concepts and functionalities
Performance features will be covered later

## Slide 25: CUDA – C with no shader limitations!
Integrated host+device app C program
  Serial or modestly parallel parts in host C code
  Highly parallel parts in device SPMD/SIMT kernel C code
Serial Code (host)‏
. . .
. . .
Parallel Kernel (device)‏
KernelA<<< nBlk, nTid >>>(args);
Serial Code (host)‏
Parallel Kernel (device)‏
KernelB<<< nBlk, nTid >>>(args);
Notes: Sequential part often overlapped with parallel part

## Slide 26: CUDA Devices and Threads
A compute device
  Is a coprocessor to the CPU or host
  Has its own DRAM (device memory)‏
  Runs many threads in parallel
  Is typically a GPU but can also be another type of parallel processing device
Data-parallel portions of an application are expressed as device kernels which run on many threads
Differences between GPU and CPU threads
  GPU threads are extremely lightweight
    Very little creation overhead
  GPU needs 1000s of threads for full efficiency
    Multi-core CPU needs only a few
Notes: MCUDA tool can be used to utilize multicore CPU’s instead of GPU
Very small time to create GPU threads; done in hardware in a few cycles

## Slide 27: G80 CUDA mode – A Device Example
Processors execute computing threads
New operating mode/HW interface for computing
Load/store
Global Memory
Thread Execution Manager
Input Assembler
Host
Texture
Texture
Texture
Texture
Texture
Texture
Texture
Texture
Texture
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Load/store
Load/store
Load/store
Load/store
Load/store

## Slide 28: Extended C
Type Qualifiers
  global, device, shared, local, host
Keywords
  threadIdx, blockIdx
Intrinsics
  __syncthreads
Runtime API
  Memory, symbol, execution management
Function launch
__device__ float filter[N];
__global__ void convolve (float *image) {
__shared__ float region[M];
...
region[threadIdx] = image[i];
__syncthreads()
...
image[j] = result;
}
// Allocate GPU memory
void *myimage = cudaMalloc(bytes)
// 100 blocks, 10 threads per block
convolve<<<100, 10>>> (myimage);

## Slide 29: CUDA Platform

## Slide 30: CUDA Platform

## Slide 31
Arrays of Parallel Threads
A CUDA kernel is executed by an array of threads
  All threads run the same code (SPMD)‏
  Each thread has an ID that it uses to compute memory addresses and make control decisions
7
6
5
4
3
2
1
0
…
float x = input[threadID];
float y = func(x);
output[threadID] = y;
…
threadID

## Slide 32: Thread Blocks: Scalable Cooperation
…
float x = input[threadID];
float y = func(x);
output[threadID] = y;
…
threadID
Thread Block 0
…
…
float x = input[threadID];
float y = func(x);
output[threadID] = y;
…
Thread Block 1
…
float x = input[threadID];
float y = func(x);
output[threadID] = y;
…
Thread Block N - 1
Divide monolithic thread array into multiple blocks
  Threads within a block cooperate via shared memory, atomic operations and barrier synchronization
  Threads in different blocks cannot cooperate
  Up to 65535 blocks, 512 threads/block
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
Notes: Analogy to street addresses

## Slide 33: Block IDs and Thread IDs
We launch a “grid” of “blocks” of “threads”
Each thread uses IDs to decide what data to work on
  Block ID: 1D, 2D, or 3D
    Usually 1D or 2D
  Thread ID: 1D, 2D, or 3D
Simplifies memory addressing when processing multidimensional data
  Image processing
  Solving PDEs on volumes
  …

## Slide 34: CUDA Memory Model Overview
Global memory
  Main means of communicating R/W Data between host and device
  Contents visible to all threads
  Long latency access
We will focus on global memory for now
  Constant and texture memory will come later
Grid
Global Memory
Block (0, 0)‏
Shared Memory
Thread (0, 0)‏
Registers
Thread (1, 0)‏
Registers
Block (1, 0)‏
Shared Memory
Thread (0, 0)‏
Registers
Thread (1, 0)‏
Registers
Host

## Slide 35: CUDA Device Memory Allocation
cudaMalloc()
  Allocates object in the device Global Memory
  Requires two parameters
    Address of a pointer to the allocated object
    Size of allocated object
cudaFree()
  Frees object from device Global Memory
    Pointer to freed object
Grid
Global
Memory
Block (0, 0)‏
Shared Memory
Thread (0, 0)‏
Registers
Thread (1, 0)‏
Registers
Block (1, 0)‏
Shared Memory
Thread (0, 0)‏
Registers
Thread (1, 0)‏
Registers
Host
    DON’T use a CPU pointer in a GPU function !

## Slide 36: CUDA Device Memory Allocation (cont.)‏
Code example:
  Allocate a 64 * 64 single precision float array
  Attach the allocated storage to Md
  “d” is often used to indicate a device data structure
TILE_WIDTH = 64;
float* Md;
int size = TILE_WIDTH * TILE_WIDTH * sizeof(float);
cudaMalloc((void**)&Md, size);
cudaFree(Md);

## Slide 37: CUDA Host-Device Data Transfer
cudaMemcpy()
  memory data transfer
  Requires four parameters
    Pointer to destination
    Pointer to source
    Number of bytes copied
    Type of transfer
      Host to Host
      Host to Device
      Device to Host
      Device to Device
Non-blocking/asynchronous transfer
Grid
Global
Memory
Block (0, 0)‏
Shared Memory
Thread (0, 0)‏
Registers
Thread (1, 0)‏
Registers
Block (1, 0)‏
Shared Memory
Thread (0, 0)‏
Registers
Thread (1, 0)‏
Registers
Host

## Slide 38: CUDA Host-Device Data Transfer (cont.)
Code example:
  Transfer a 64 * 64 single precision float array
  M is in host memory and Md is in device memory
  cudaMemcpyHostToDevice and cudaMemcpyDeviceToHost are symbolic constants
cudaMemcpy(Md, M, size, cudaMemcpyHostToDevice);
cudaMemcpy(M, Md, size, cudaMemcpyDeviceToHost);

## Slide 39: CUDA Keywords

## Slide 40: CUDA Function Declarations
host
host
__host__ float HostFunc()‏
host
device
__global__ void KernelFunc()‏
device
device
__device__ float DeviceFunc()‏
Only callable from the:
Executed on the:
__global__ defines a kernel function
  Must return void

## Slide 41: CUDA Function Declarations (cont.)‏
__device__ functions cannot have their address taken
For functions executed on the device:
  No recursion
  No static variable declarations inside the function
  No variable number of arguments

## Slide 42: Calling a Kernel Function – Thread Creation
A kernel function must be called with an execution configuration:
__global__ void KernelFunc(...);
dim3 DimGrid(100, 50); // 5000 thread blocks
dim3 DimBlock(4, 8, 8); // 256 threads per block
size_t SharedMemBytes = 64; // 64 bytes of shared memory
KernelFunc<<< DimGrid, DimBlock, SharedMemBytes >>>(...);
Any call to a kernel function is asynchronous from CUDA 1.0 on, explicit synch needed for blocking

## Slide 43: Next Time
Code example