## Slide 1: Instruction-Level Parallelism Dynamic Scheduling
CS448

## Slide 2: Dynamic Scheduling
Static Scheduling – Compiler rearranging instructions to reduce stalls
Dynamic Scheduling – Hardware rearranges instruction stream to reduce stalls
  Possible to account for dependencies that are only known at run time - e. g. memory reference
  Simplifies the compiler
  Code built for one pipeline in mind could also run efficiently on a different pipeline
  minimizes the need for speculative slot filling - NP hard
Once a common tactic with supercomputers and mainframes but was too expensive for single-chip
  Now fits on a desktop PC’s

## Slide 3: Dynamic Scheduling
Dependencies that are close together stall the entire pipeline
  DIVD F0, F2, F4
  ADDD F10, F0, F8
  SUBD F12, F8, F14
The ADD needs the DIV to finish, so there is a stall… which also stalls the SUBD
  Looong stall for DIV
  But the SUBD is independent so there is no reason why we shouldn’t execute it
  Or is there?
    Precise Interrupts - Ignore for now
Compiler could rearrange instructions, but so could the hardware

## Slide 4: Dynamic Scheduling
It would be desirable to decode instructions into the pipe in order but then let them stall individually while waiting for operands before issue to execution units.
Dynamic Scheduling – Out of Order Issue / Execution
Scoreboarding

## Slide 5: Scoreboarding
Split ID stage into two:
Issue (Decode, check for Structural hazards)
Read Operands (Wait until no data hazards, read operands)

## Slide 6: Scoreboard Overview
Consider another example:
  DIVD F0, F2, F4
  ADDD F10, F0, F8 ; RAW Hazard
  SUBD F8, F8, F14 ; WAR Hazard
Note:
  We may still have to stall in the Scoreboard
  SUBD wouldn’t have to wait if we had a different register other than F8
MIPS Pipeline changes again
  Ignore MEM and IF stages for now to focus on the scoreboard

## Slide 7: Scoreboard and the CDC
Introduced on CDC 6600
  4 Floating Point Units, 5 Memory, 7 Integer Units
  Load/Store architecture
Results
  70 to 150% improvement
    Good since this cost over $1 million
  Recall this is an old machine with no cache, pipelining, primitive compilers
  Fastest machine of the time
Back today in IBM, Sun machines, similar concepts in Intel chips

## Slide 8: MIPS Scoreboard
Two MULT units
Note: Need a lot
more buses

## Slide 9: New Pipeline Steps
Ignoring IF, and MEM
Issue
  If functional unit free and no other active instruction has the same destination register, issue the instruction to the functional unit
  Stall for WAW hazards or structural hazards
  Nothing out of order yet
Read Operands
  Monitor source operands, if available for an active instruction, then send to the functional unit to execute
  Instructions get out of order at this step, dynamic RAW resolution
Execution
  Starts when operands ready, notifies scoreboard when done
Write Result
  Stall for WAR hazards before writing result back to register file
IF
EX
WB

## Slide 10: Scoreboard Data Structure
Instruction Status
  Indicates which of the four steps the instruction is in (Issue, Read Operands, Execute Complete, Write Result)
  The capacity of the instruction status is the window size
Functional Unit Status
  Busy : Yes/No indicates if busy or not
  Op: Operation to perform, e.g. Add or Subtract
  Fi : Destination Register
  Fj, Fk : Source Registers
  Qj, Qk : Functional Units producing source register j, k
  Rj, Rk : Yes/No indicates if source j or k is ready or not, set to NO after operands are read
Register Result Status
  For each register, indicates the Functional Unit that will write to it
  Blank means nothing will write to it
  Note overlap of this info with Q/F fields, but indexed by register, not instr

## Slide 11: Example Scoreboard

## Slide 12: Scoreboard Example
Assume the following EX latencies
  FP Add = 2 clock cycles
  FP Mult = 10 clock cycles
  FP Div = 40 clock cycles
Assume entire code fragment (basic block) fits in the window
  Also assume the code fragment is already loaded
Issue Rules
  Issue maximum 1 instruction per cycle
  Clearing hazards will depend on the pipeline structure

## Slide 13: MIPS Scoreboarding Rules
Issue
  If FU not busy (no structural hazards) and no result pending for destination register (no WAW hazards) then
    Assign FU entry
    Set operand source in scoreboard, indicate if ready or not
Read Operands
  If source1 and source2 are both “ready” (no RAW hazards) then
    Set ready=No for both, read registers, and start EX
Execute
  Notify scoreboard when complete
Writeback
  If none of the functional units needs to use our result register and has yet to read it (no WAR hazards) then
    Set ready=Yes for any functional unit sources waiting for this FU
    write the register file, clear the FU status, and clear our destination’s register result pending entry.
Stages must stall for hazards

## Slide 14: Scoreboard – Cycle 1
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 |  |  | 
LD F2, 45(R3) |  |  |  | 
MULTD F0, F2, F4 |  |  |  | 
SUBD F8, F6, F2 |  |  |  | 
DIVD, F10, F0, F6 |  |  |  | 
ADDD F6, F8, F2 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | Yes | LD | F6 |  | R2 |  |  |  | Yes
Mult1 |  |  |  |  |  |  |  |  | 
Mult2 |  |  |  |  |  |  |  |  | 
Add |  |  |  |  |  |  |  |  | 
Divide |  |  |  |  |  |  |  |  | 
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU |  |  |  | Int |  |  |  |  | 
IS
FS
RRS

## Slide 15: Scoreboard – Cycle 2
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 |  | 
LD F2, 45(R3) |  |  |  | 
MULTD F0, F2, F4 |  |  |  | 
SUBD F8, F6, F2 |  |  |  | 
DIVD, F10, F0, F6 |  |  |  | 
ADDD F6, F8, F2 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | Yes | LD | F6 |  | R2 |  |  |  | Yes
Mult1 |  |  |  |  |  |  |  |  | 
Mult2 |  |  |  |  |  |  |  |  | 
Add |  |  |  |  |  |  |  |  | 
Divide |  |  |  |  |  |  |  |  | 
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU |  |  |  | Int |  |  |  |  | 
IS
FS
RRS
Issue 2nd LD?

## Slide 16: Scoreboard – Cycle 3
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 
LD F2, 45(R3) |  |  |  | 
MULTD F0, F2, F4 |  |  |  | 
SUBD F8, F6, F2 |  |  |  | 
DIVD, F10, F0, F6 |  |  |  | 
ADDD F6, F8, F2 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | Yes | LD | F6 |  | R2 |  |  |  | No
Mult1 |  |  |  |  |  |  |  |  | 
Mult2 |  |  |  |  |  |  |  |  | 
Add |  |  |  |  |  |  |  |  | 
Divide |  |  |  |  |  |  |  |  | 
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU |  |  |  | Int |  |  |  |  | 
IS
FS
RRS
Issue Mult?

## Slide 17: Scoreboard – Cycle 4
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) |  |  |  | 
MULTD F0, F2, F4 |  |  |  | 
SUBD F8, F6, F2 |  |  |  | 
DIVD, F10, F0, F6 |  |  |  | 
ADDD F6, F8, F2 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | Yes | LD | F6 |  | R2 |  |  |  | No
Mult1 |  |  |  |  |  |  |  |  | 
Mult2 |  |  |  |  |  |  |  |  | 
Add |  |  |  |  |  |  |  |  | 
Divide |  |  |  |  |  |  |  |  | 
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU |  |  |  |  |  |  |  |  | 
IS
FS
RRS

## Slide 18: Scoreboard – Cycle 5
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 |  |  | 
MULTD F0, F2, F4 |  |  |  | 
SUBD F8, F6, F2 |  |  |  | 
DIVD, F10, F0, F6 |  |  |  | 
ADDD F6, F8, F2 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | Yes | LD | F2 |  | R3 |  |  |  | Yes
Mult1 |  |  |  |  |  |  |  |  | 
Mult2 |  |  |  |  |  |  |  |  | 
Add |  |  |  |  |  |  |  |  | 
Divide |  |  |  |  |  |  |  |  | 
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU |  | Int |  |  |  |  |  |  | 
IS
FS
RRS

## Slide 19: Scoreboard – Cycle 6
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 |  | 
MULTD F0, F2, F4 | 6 |  |  | 
SUBD F8, F6, F2 |  |  |  | 
DIVD, F10, F0, F6 |  |  |  | 
ADDD F6, F8, F2 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | Yes | LD | F2 |  | R3 |  |  |  | Yes
Mult1 | Yes | Mult | F0 | F2 | F4 | Int |  | No | Yes
Mult2 |  |  |  |  |  |  |  |  | 
Add |  |  |  |  |  |  |  |  | 
Divide |  |  |  |  |  |  |  |  | 
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU | Mul | Int |  |  |  |  |  |  | 
IS
FS
RRS

## Slide 20: Scoreboard – Cycle 7
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 
MULTD F0, F2, F4 | 6 |  |  | 
SUBD F8, F6, F2 | 7 |  |  | 
DIVD, F10, F0, F6 |  |  |  | 
ADDD F6, F8, F2 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | Yes | LD | F2 |  | R3 |  |  |  | No
Mult1 | Yes | Mult | F0 | F2 | F4 | Int |  | No | Yes
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Sub | F8 | F6 | F2 |  | Int | Yes | No
Divide |  |  |  |  |  |  |  |  | 
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU | Mul | Int |  |  | Add |  |  |  | 
IS
FS
RRS
Read Mult operands?

## Slide 21: Scoreboard – Cycle 8a
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 
MULTD F0, F2, F4 | 6 |  |  | 
SUBD F8, F6, F2 | 7 |  |  | 
DIVD, F10, F0, F6 | 8 |  |  | 
ADDD F6, F8, F2 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | Yes | LD | F2 |  | R3 |  |  |  | No
Mult1 | Yes | Mult | F0 | F2 | F4 | Int |  | No | Yes
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Sub | F8 | F6 | F2 |  | Int | Yes | No
Divide | Yes | Div | F10 | F0 | F6 | Mul1 |  | No | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU | Mul | Int |  |  | Add | Div |  |  | 
IS
FS
RRS
Issue first

## Slide 22: Scoreboard – Cycle 8b
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 |  |  | 
SUBD F8, F6, F2 | 7 |  |  | 
DIVD, F10, F0, F6 | 8 |  |  | 
ADDD F6, F8, F2 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | Yes | LD | F2 |  | R3 |  |  |  | No
Mult1 | Yes | Mult | F0 | F2 | F4 |  |  | Yes | Yes
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Sub | F8 | F6 | F2 |  |  | Yes | Yes
Divide | Yes | Div | F10 | F0 | F6 | Mul1 |  | No | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU | Mul |  |  |  | Add | Div |  |  | 
IS
FS
RRS
Write result

## Slide 23: Scoreboard – Cycle 9
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 |  | 
SUBD F8, F6, F2 | 7 | 9 |  | 
DIVD, F10, F0, F6 | 8 |  |  | 
ADDD F6, F8, F2 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | Yes | Mult | F0 | F2 | F4 |  |  | Yes | Yes
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Sub | F8 | F6 | F2 |  |  | Yes | Yes
Divide | Yes | Div | F10 | F0 | F6 | Mul1 |  | No | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU | Mul |  |  |  | Add | Div |  |  | 
IS
FS
RRS
Issue ADD?

## Slide 24: Scoreboard – Cycle 10
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 |  | 
SUBD F8, F6, F2 | 7 | 9 |  | 
DIVD, F10, F0, F6 | 8 |  |  | 
ADDD F6, F8, F2 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | Yes | Mult | F0 | F2 | F4 |  |  | No | No
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Sub | F8 | F6 | F2 |  |  | No | No
Divide | Yes | Div | F10 | F0 | F6 | Mul1 |  | No | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU | Mul |  |  |  | Add | Div |  |  | 
IS
FS
RRS
Exec MULT, ADD

## Slide 25: Scoreboard – Cycle 11
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 |  | 
SUBD F8, F6, F2 | 7 | 9 | 11 | 
DIVD, F10, F0, F6 | 8 |  |  | 
ADDD F6, F8, F2 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | Yes | Mult | F0 | F2 | F4 |  |  | No | No
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Sub | F8 | F6 | F2 |  |  | No | No
Divide | Yes | Div | F10 | F0 | F6 | Mul1 |  | No | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU | Mul |  |  |  | Add | Div |  |  | 
IS
FS
RRS

## Slide 26: Scoreboard – Cycle 12
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 |  | 
SUBD F8, F6, F2 | 7 | 9 | 11 | 12
DIVD, F10, F0, F6 | 8 |  |  | 
ADDD F6, F8, F2 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | Yes | Mult | F0 | F2 | F4 |  |  | No | No
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Sub | F8 | F6 | F2 |  |  | No | No
Divide | Yes | Div | F10 | F0 | F6 | Mul1 |  | No | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU | Mul |  |  |  |  | Div |  |  | 
IS
FS
RRS
Read opnds DIVD?

## Slide 27: Scoreboard – Cycle 13
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 |  | 
SUBD F8, F6, F2 | 7 | 9 | 11 | 12
DIVD, F10, F0, F6 | 8 |  |  | 
ADDD F6, F8, F2 | 13 |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | Yes | Mult | F0 | F2 | F4 |  |  | No | No
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Add | F6 | F8 | F2 |  |  | Yes | Yes
Divide | Yes | Div | F10 | F0 | F6 | Mul1 |  | No | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU | Mul |  |  | Add |  | Div |  |  | 
IS
FS
RRS

## Slide 28: Scoreboard – Cycle 14
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 |  | 
SUBD F8, F6, F2 | 7 | 9 | 11 | 12
DIVD, F10, F0, F6 | 8 |  |  | 
ADDD F6, F8, F2 | 13 | 14 |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | Yes | Mult | F0 | F2 | F4 |  |  | No | No
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Add | F6 | F8 | F2 |  |  | Yes | Yes
Divide | Yes | Div | F10 | F0 | F6 | Mul1 |  | No | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU | Mul |  |  | Add |  | Div |  |  | 
IS
FS
RRS

## Slide 29: Scoreboard – Cycle 15
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 |  | 
SUBD F8, F6, F2 | 7 | 9 | 11 | 12
DIVD, F10, F0, F6 | 8 |  |  | 
ADDD F6, F8, F2 | 13 | 14 |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | Yes | Mult | F0 | F2 | F4 |  |  | No | No
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Add | F6 | F8 | F2 |  |  | No | No
Divide | Yes | Div | F10 | F0 | F6 | Mul1 |  | No | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU | Mul |  |  | Add |  | Div |  |  | 
IS
FS
RRS
Start EX on ADD

## Slide 30: Scoreboard – Cycle 16
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 |  | 
SUBD F8, F6, F2 | 7 | 9 | 11 | 12
DIVD, F10, F0, F6 | 8 |  |  | 
ADDD F6, F8, F2 | 13 | 14 | 16 | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | Yes | Mult | F0 | F2 | F4 |  |  | No | No
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Add | F6 | F8 | F2 |  |  | No | No
Divide | Yes | Div | F10 | F0 | F6 | Mul1 |  | No | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU | Mul |  |  | Add |  | Div |  |  | 
IS
FS
RRS

## Slide 31: Scoreboard – Cycle 17
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 |  | 
SUBD F8, F6, F2 | 7 | 9 | 11 | 12
DIVD, F10, F0, F6 | 8 |  |  | 
ADDD F6, F8, F2 | 13 | 14 | 16 | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | Yes | Mult | F0 | F2 | F4 |  |  | No | No
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Add | F6 | F8 | F2 |  |  | No | No
Divide | Yes | Div | F10 | F0 | F6 | Mul1 |  | No | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU | Mul |  |  | Add |  | Div |  |  | 
IS
FS
RRS
Write Result Add?

## Slide 32: Scoreboard – Cycle 19
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 | 19 | 
SUBD F8, F6, F2 | 7 | 9 | 11 | 12
DIVD, F10, F0, F6 | 8 |  |  | 
ADDD F6, F8, F2 | 13 | 14 | 16 | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | Yes | Mult | F0 | F2 | F4 |  |  | No | No
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Add | F6 | F8 | F2 |  |  | No | No
Divide | Yes | Div | F10 | F0 | F6 | Mul1 |  | No | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU | Mul |  |  | Add |  | Div |  |  | 
IS
FS
RRS

## Slide 33: Scoreboard – Cycle 20
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 | 19 | 20
SUBD F8, F6, F2 | 7 | 9 | 11 | 12
DIVD, F10, F0, F6 | 8 |  |  | 
ADDD F6, F8, F2 | 13 | 14 | 16 | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | Yes | Mult | F0 | F2 | F4 |  |  | No | No
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Add | F6 | F8 | F2 |  |  | No | No
Divide | Yes | Div | F10 | F0 | F6 | Mul1 |  | Yes | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU |  |  |  | Add |  | Div |  |  | 
IS
FS
RRS

## Slide 34: Scoreboard – Cycle 21
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 | 19 | 20
SUBD F8, F6, F2 | 7 | 9 | 11 | 12
DIVD, F10, F0, F6 | 8 | 21 |  | 
ADDD F6, F8, F2 | 13 | 14 | 16 | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | No |  |  |  |  |  |  |  | 
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Add | F6 | F8 | F2 |  |  | No | No
Divide | Yes | Div | F10 | F0 | F6 |  |  | Yes | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU |  |  |  | Add |  | Div |  |  | 
IS
FS
RRS

## Slide 35: Scoreboard – Cycle 22
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 | 19 | 20
SUBD F8, F6, F2 | 7 | 9 | 11 | 12
DIVD, F10, F0, F6 | 8 | 21 |  | 
ADDD F6, F8, F2 | 13 | 14 | 16 | 22
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | No |  |  |  |  |  |  |  | 
Mult2 |  |  |  |  |  |  |  |  | 
Add | Yes | Add | F6 | F8 | F2 |  |  | No | No
Divide | Yes | Div | F10 | F0 | F6 |  |  | Yes | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU |  |  |  |  |  | Div |  |  | 
IS
FS
RRS
Safe to write

## Slide 36: Scoreboard – Cycle 61
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 | 19 | 20
SUBD F8, F6, F2 | 7 | 9 | 11 | 12
DIVD, F10, F0, F6 | 8 | 21 | 61 | 
ADDD F6, F8, F2 | 13 | 14 | 16 | 22
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | No |  |  |  |  |  |  |  | 
Mult2 |  |  |  |  |  |  |  |  | 
Add | No |  |  |  |  |  |  |  | 
Divide | Yes | Div | F10 | F0 | F6 |  |  | Yes | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU |  |  |  |  |  | Div |  |  | 
IS
FS
RRS

## Slide 37: Scoreboard – Cycle 62
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F6, 34(R2) | 1 | 2 | 3 | 4
LD F2, 45(R3) | 5 | 6 | 7 | 8
MULTD F0, F2, F4 | 6 | 9 | 19 | 20
SUBD F8, F6, F2 | 7 | 9 | 11 | 12
DIVD, F10, F0, F6 | 8 | 21 | 61 | 62
ADDD F6, F8, F2 | 13 | 14 | 16 | 22
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | No |  |  |  |  |  |  |  | 
Mult1 | No |  |  |  |  |  |  |  | 
Mult2 |  |  |  |  |  |  |  |  | 
Add | No |  |  |  |  |  |  |  | 
Divide | Yes | Div | F10 | F0 | F6 |  |  | Yes | Yes
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU |  |  |  |  |  |  |  |  | 
IS
FS
RRS

## Slide 38
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F2, 0(R1) |  |  |  | 
ADDD F6, F2, F4 |  |  |  | 
MULTD F8, F6, F0 |  |  |  | 
LD F10, -8(R1) |  |  |  | 
ADDD, F12, F10, F4 |  |  |  | 
MULTD F14, F12,F0 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer |  |  |  |  |  |  |  |  | 
Integer |  |  |  |  |  |  |  |  | 
Mult |  |  |  |  |  |  |  |  | 
Add |  |  |  |  |  |  |  |  | 
Add |  |  |  |  |  |  |  |  | 
Divide |  |  |  |  |  |  |  |  | 
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU |  |  |  |  |  |  |  |  | 
IS
FS
RRS

## Slide 39
Instr | Issue | Read Operands | Exec Complete | Write Result
LD F2, 0(R1) | 1 | 2 | 3 | 4
ADDD F6, F2, F4 | 2 | 5 | 7 | 8
MULTD F8, F6, F0 | 3 | 9 | 19 | 20
LD F10, -8(R1) | 4 | 5 | 6 | 7
ADDD, F12, F10, F4 | 5 | 8 | 10 | 11
MULTD F14, F12,F0 | 21 | 22 | 32 | 33
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Integer | Y | Load | F2 | R1 |  |  |  | Yes | 
Integer | Y | Load | F10 | R1 |  |  |  | Yes | 
Mult | Y | Mult | F8 | F6 | F0 | Add1 |  | Yes | Yes
Add | Y | Add | F6 | F2 | F4 | Int1 |  | Yes | Yes
Add | Y | Add | F12 | F10 | F4 | Int2 |  | No | Yes
Divide |  |  |  |  |  |  |  |  | 
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | F14 | F30
FU |  |  |  |  | Mult1 | Int2 | Add2 |  | 

## Slide 40
Instr | Issue | Read Operands | Exec Complete | Write Result
DIVD F10, F8, F2 |  |  |  | 
ADDD F4, F10, F2 |  |  |  | 
LD F2, 8(R0) |  |  |  | 
ADDD F6, F0, F12 |  |  |  | 
Name | Busy | Op | Fi | Fj | Fk | Qj | Qk | Rj | Rk
Int1 |  |  |  |  |  |  |  |  | 
Int2 |  |  |  |  |  |  |  |  | 
Mult |  |  |  |  |  |  |  |  | 
Add |  |  |  |  |  |  |  |  | 
Divide |  |  |  |  |  |  |  |  | 
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
FU |  |  |  |  |  |  |  |  | 
IS
FS
RRS

## Slide 41: Scoreboarding Comments
Could improve a bit with forwarding
  Improve by one cycle for forwarded data
Whats Missing
  Control Hazards, i.e. branches
    Dynamic Branch Prediction
    Speculative Execution
Limitations
  Note we had to wait for a register to be read before writing
    Could be avoided with Register Renaming
  Amount of ILP limited by RAW hazards
    Some estimate the amount of parallelism typically ~2
  Window Size
  Number and Type of Functional Units, Lots of Buses
  Big increase in cost and complexity!

## Slide 42: Static Scheduling Revisited
Scoreboarding stalled for WAR and WAW hazards
Consider the fragment
  DIVD F1, F2, F3 ; slow
  SUBD F2, F3, F4 ; must wait for DIV to read, WAR
  SD 0(R1), F2
  There is a WAR antidependence on F2 between the DIV and the SUB.
By “renaming” F2 and subsequent uses of it we avoid the hazard
  DIVD F1, F2, F3 ; slow
  SUBD F5, F3, F4 ; Free to start anytime
  SD 0(R1), F5
Reduces stalls for some pipelines, but uses additional registers

## Slide 43: Dynamic Scheduling
Same idea as before, but in hardware, not software
Every time you write to a register number, allocate a new physical register from a pool of virtual registers. Results in multiple copies of each register, one for each new value written to it.
Implementation implications:
  Need more physical registers than register addresses
  Keep a pool of unassigned physical registers, and allocate one when a register is written
  All uses to the original register number must be remapped to the new physical register
  When a register is written, all previous physical registers allocated for it can be freed as soon as all previous instructions that use it have completed
Can eliminate stalls for WAR and WAW hazards

## Slide 44: Register Renaming Idea
Initial mappings:
  F1  V1
  F2  V2
  F3  V3
  F4  V4
DIVD F1, F2, F3 F1  V5
SUBD F2, F3, F4 F2  V6
ADDD F1, F3, F2 F1  V7
Becomes
DIVD V5, V2, V3
SUBD V6, V3, V4
ADDD V7, V3, V6 Note V6 here not V2

## Slide 45: Tomasulo’s Algorithm
Uses register renaming
Idea:
  When opcode, operands, and functional unit is available, execute the instruction, data-centric
Replace the Functional Unit Status table with reservation stations for each functional unit
  The reservation station stores operand values as they become available, or the name of a reservation station that will provide the result. This means that the original register number is no longer needed, and is now “renamed” as a reservation station
Each result is broadcast to any reservation station that needs it
Instructions can now be issued even if there are structural hazards or WAR/WAW hazards.

## Slide 46: MIPS FP via Tomasulo
Tags
Notes: Need more reservation stations than actual registers

## Slide 47: Tomasulo vs. Scoreboarding
Tomasulo’s Algorithm
  Used on IBM 360
  attempt to deal with long memory and FP latencies
  360 permitted register to memory ALU instructions
vs. CDC scoreboard
  hazard detection and interlocks are distributed
    Each functional unit has reservation stations to control execution
    Reservation stations act as interlocks until data available
  Results passed directly to functional units rather than through the registers (with renamed registers) multicast on CDB (common data bus)
Dataflow centric
  no WAR or WAW hazards exist - rename instead
  Scoreboard was control centric

## Slide 48: Tomasulo - Central Idea
To speed up the 360 we can
  Add more functional units, but they wouldn’t be heavily used
  Replicating registers is cheaper and increases utilization
  Helped on 360 which had only 6 FP registers (similar to x86)
Outcome
  each execution unit fed by multiple reservation stations
  Execution units used pipelining
  Instruction issue to reservation stations is in-order, but reservation stations would execute upon acquiring all source operands  out of order execution
  reservation stations contain virtual registers that remove WAW and WAR induced stalls

## Slide 49: Dynamic Scheduling
Both Scoreboarding and Tomasulo’s algorithm were early approaches, but the ideas are still used today
  Scoreboarding - CDC 6600 (1964)
  Tomasulo - IBM 360/ 91 (1967)
Both methods are used today
  UltraSparc
  Pentium/Itanium
    More transistors dedicated to ILP in the original Pentium than in the entire 486