## Slide 1: Synchronization

## Slide 2: Synchronization
How to synchronize processes?
  Need to protect access to shared data to avoid problems like race conditions
  Typical example: Updating a shared account balance. Problem below?
Processor 1
lw $t0,balance
lw $t1,amount
add $t0,$t0,t1
sw $t0,balance
Processor 2
lw $t2,balance
lw $t3,amount
sub $t2,$t2,t3
sw $t2,balance

## Slide 3: Critical Sections
In general:
  n processes all competing to use some shared data
  Each process has a critical section in which shared data is accessed
Goal
  Ensure that when one process is executing in its critical section, no other process is allowed to execute in its critical section
Processor
Entry_section() // Wait until exclusive access
Critical Section
Remainder_section() // Release exclusivity

## Slide 4: Criteria for Critical Sections
Mutual exclusion
  Two processors can never be in the critical section at the same time
Progress
  If no process is executing in its critical section and some processes wish to enter their critical sections, then only those processes that are not executing in their remainder sections can participate in the decision on which will enter its critical section next.
Bounded waiting
  There exists a bound or limit on the number of times that other processes are allowed to enter their critical sections after a process has made a request to enter its critical section and before that request is granted

## Slide 5: First Attempt - Alternation
Processor 0
shared int turn = 0;
while (turn != 0);
Critical Section
turn = 1;
Remainder_section()
Processor 1
shared int turn = 0;
while (turn != 1);
Critical Section
turn = 0;
Remainder_section()
Satisfies mutual exclusion
Does not satisfy progress
Might satisfy bounded wait if processors eventually set the turn variable

## Slide 6: Second Attempt – Warning Flags
Processor 0
shared int flag[2] = {0,0};
flag[0] = TRUE;
while (flag[1]);
Critical Section
flag[0] = FALSE;
Remainder_section()
Satisfies mutual exclusion and progress
P0 only enters critical section if flag[0] && !flag[1]
P1 only enters critical section if flag[1] && !flag[0]
Satisfy bounded wait? Deadlock possible?
Processor 1
shared int flag[2] = {0,0};
flag[1] = TRUE;
while (flag[0]);
Critical Section
flag[1] = FALSE;
Remainder_section()

## Slide 7: Software Solution – Peterson’s Algorithm
Processor 0
shared int flag[2] = {0,0};
shared int turn;
flag[0] = TRUE;
turn = 1;
while (turn == 1 && flag[1]);
Critical Section
flag[0] = FALSE;
Remainder_section()
Processor 1
shared int flag[2] = {0,0};
shared int turn;
flag[1] = TRUE;
turn = 0;
while (turn == 0 && flag[0]);
Critical Section
flag[1] = FALSE;
Remainder_section()
Combines alternation and warning flags
Polite – we want to enter, but if someone else wants to enter, go ahead
Satisfies mutual exclusion, progress, and bounded wait
Slow (busy wait) and unwieldy to extend to many processors

## Slide 8: Hardware Synchronization
For large scale MPs, synchronization can be a bottleneck
  Contention adds additional delays, latency is potentially great
Hardware primitives needed
  all solutions based on "atomically inspect and update a memory location"
Higher level synchronization solutions can be build on top of the basic hardware primitives
  Locks, barriers
  Generally employed by the system software not the programmer directly

## Slide 9: Uninterruptible Instructions to Fetch and Write to Memory
Atomic exchange: interchange a value in a register for a value in memory
  Used to build a simple lock
  To lock, set register to 1 and exchange
    0 => synchronization variable is free
    1 => synchronization variable is locked by some other processor and unavailable
  Must be atomic or synchronization may fail
Test-and-set: tests a value and sets it if the value passes the test
  Ex. Test for 0 and if so set to 1
Fetch-and-increment: it returns the value of a memory location and atomically increments it
  0 => synchronization variable is free
All implementations require coherence

## Slide 10: A spin lock using the exchange primitive
Spin locks: processor continuously tries to acquire, spinning around a loop trying to get the lock:
LI R2,#1 ;load immediate lock: EXCH R2,0(R1) ;atomic exchange BNEZ R2,lock ;already locked?
Multiprocessors with cache coherency
  Want to spin on cache copy to avoid full memory latency
  Likely to get cache hits for such variables
  Problem: exchange includes a write, which invalidates all other copies; this generates considerable bus traffic
  Solution: start by simply repeatedly reading the variable; when it changes, then try exchange (“test and test & set”):
try: LI R2,#1 ;load immediate lock: LW R3,0(R1) ;load var BNEZ R3,lock ;not free=>spin EXCH R2,0(R1) ;atomic exchange BNEZ R2,try ;already locked?

## Slide 11: Load Linked / Store Conditional
Challenging to implement a single atomic memory operation
  Has to do a memory read and a write
  Complicates coherence since the hardware cannot allow any other operations between the read and the write
Alternative
  Have a pair of instructions, a load and a store
  The second instruction returns a value from which it can deduced if the pair executed as if it were atomic
  The load is a special load called load linked or load locked and the special store is called store conditional

## Slide 12: Load Linked / Store Conditional
If the contents of the memory location specified by the load linked are changed before the store conditional occurs, then the store conditional fails
If the processor does a context switch between the two instructions then the store conditional fails
Store conditional returns 1 if successful and 0 otherwise

## Slide 13: Examples with LL/SC
Atomic swap with LL & SC on memory location specified by R1
try: MOV R3, R4 ; Mov Exchange value
LL R2, 0(R1) ; Load Linked
SC R3, 0(R1) ; Store Conditional
BEQZ R3, try ; Branch store fails
MOV R4, R2 ; Put load value in R4
If SC fails then R3 = 0 and we branch and try again (e.g. a processor intervened
and modified the value in 0(R1)).
Atomic fetch and increment:
try: LL R2, 0(R1) ; Load Linked
DADDUI R3, R2, #1 ; Increment
SC R3, 0(R1) ; Store Conditional
BEQZ R3, try ; Branch store fails

## Slide 14: Implementing LL/SC
Link Register
  Stores the address specified in the LL instruction
Interrupt or Cache block matching the link register is invalidated
  Clear the link register
  Same idea as snooping, listening for a write on the address of the link register
Some care must be taken; deadlock conditions possible depending upon what is placed between LL and SC (should only be register-register instructions)

## Slide 15: Barrier Synchronization
All must arrive before any can leave
  Used between different parallel sections
Uses two shared variables
  A counter that counts how many have arrived
  A flag that is set when the last processor arrives

## Slide 16: Simple Barrier Synchronization
lock();
if(count==0) release=FALSE; /* First resets release */
count++; /* Count arrivals */
unlock();
if(count==total) /* All arrived */
{
count=0; /* Reset counter */
release = TRUE; /* Release processes */
}
else /* Wait for more to come */
{
while (!release); /* Wait for release */
}
Problem: deadlock possible if reused
  Two processes: fast and slow
  Slow arrives first, reads release, sees FALSE
  Fast arrives, sets release to TRUE, goes on to execute other code, comes to barrier again, resets release to FALSE, starts spinning on wait for release
  Slow now reads release again, sees FALSE again
  Now both processors are stuck and will never leave

## Slide 17: Correct Barrier Synchronization
localSense=!localSense; /* Toggle local sense */
lock();
count++; /* Count arrivals */
if(count==total){ /* All arrived */
count=0; /* Reset counter */
release=localSense; /* Release processes */
}
unlock();
while(release!=localSense); /* Wait to be released */
Release in first barrier acts as reset for second
  When fast comes back it does not change release, it just waits for it to become FALSE
  Slow eventually sees release is TRUE, stops waiting, does work, comes back, sets release to FALSE, and both go forward.
initially localSense = FALSE, release = FALSE

## Slide 18: Large-Scale Systems: Barriers
Barrier with many processors
  Have to update counter one by one – takes a long time
  Solution: use a combining tree of barriers
    Example: using a binary tree
    Pair up processors, each pair has its own barrier
      E.g. at level 1 processors 0 and 1 synchronize on one barrier, processors 2 and 3 on another, etc.
    At next level, pair up pairs
      Processors 0 and 2 increment a count a level 2, processors 1 and 3 just wait for it to be released
      At level 3, 0 and 4 increment counter, while 1, 2, 3, 5, 6, and 7 just spin until this level 3 barrier is released
      At the highest level all processes will spin and a few “representatives” will be counted.
    Works well because each level fast and few levels
      Only 2 increments per level, log2(numProc) levels
      For large numProc, 2*log2(numProc) still reasonably small

## Slide 19: Large-Scale Systems: Locks
Contention even with test-and-test-and-set
  Every write goes to many, many spinning procs
  Making everybody test less often reduces contention for high-contention locks but hurts for low-contention locks
  Solution: exponential back-off
    If we have waited for a long time, lock is probably high-contention
    Every time we check and fail, double the time between checks
      Fast low-contention locks (checks frequent at first)
      Scalable high-contention locks (checks infrequent in long waits)
  Special hardware support

## Slide 20: Memory Consistency
  When does a processors see another processor’s written value?
    Do different processors see writes at the same time?
    If writes are immediately seen by other processors it will be impossible for both if statements to evaluate as true
    Suppose write invalidate is delayed then it is possible P1 or P2 have not seen the invalidations before attempting to read the values
      Should this be allowed?
P1: A = 0;
…
A = 1;
L1: if (B == 0) …
P2: B = 0;
…
B = 1;
L2: if (A == 0) …

## Slide 21: Sequential Consistency
Lamport (1979): A multiprocessor is sequentially consistent if the result of any execution is the same as if the (memory) operations of all processors were executed in some sequential order, and the operations of each individual processor occur in this sequence in the order specified by its program
All processors see all loads/stores happening in the same order

## Slide 22: Sequential Consistency
Simple implementation
  A processor issues next access only when its previous access is complete
  Under sequential consistency, we cannot place the write in a write buffer and continue
  Slow
Better performance
  Latency hiding techniques
  Less restrictive memory consistency models

## Slide 23: Relaxed Consistency Models
Synchronized programs
  A program is synchronized if all access to shared data are ordered by synchronization operations
  Any two of accesses to the same variable in two different processes, such that at least one of the accesses is a write, are always ordered by synchronization operations
If variables may be updated without synchronization
  Data race and outcome is unpredictable
  Goal is data-race-free
Good performance even in simple implementation
  Seems acceptable to programmers
  Accepted that most programs are synchronized and behaves as if the hardware implemented sequential consistency

## Slide 24: Relaxed Consistency Models
There are many other relaxed models
  Processor Consistency, Partial Store Order, Release Consistency, Lazy Release Consistency
  All work just fine for data-race-free programs
  But when there are data races, more relaxed models  weird program behavior