## Slide 1: CS 470 Project Report Covering Work Completed While Employed At Scientific Fishery Systems, Inc.

## Slide 2: This Presentation
Because my time is limited to a brief 15 minutes, I am going to focus this presentation on:
  Project Background: What I worked on and the reason why it is actually useful.
  Project Design Overview: What I decided to build and why I decided to build it.
  Conclusion/Further Work: Related work that I will be involved in.
  Questions???

## Slide 3: Fish Tracking Integration
For my CS470 project I integrated echo tracking into the SciFish 2000 broadband sonar.
Tracking is important to fisheries managers because they use sonar tracks to count fish. (1 track = 1 fish)
My project was completed while working at Scientific Fishery Systems during the summer of 2002 and is a part of a larger broadband tracker project.
Financial support was provided as part of a phase II grant by the NSF’s SBIR program.

## Slide 4: Scientific Fishery Systems
Two Excerpts From The Company Website:
“Scientific Fishery Systems, Inc. (SciFish) is a customer focused, global enterprise principally engaged in the research, design, development, manufacture and integration of advanced technology systems, products, and services for government and commercial customers.”
“The Corporation's core business areas are sonar products and information systems.”
Notes: Flip Side – Stronger in Research than in Productization

## Slide 5: Background: Counting Fish
Tagging and narrowband sonar are currently the most important methods for measuring fish passage rates. Both methodologies, as currently employed, have significant drawbacks.
  Tagging can be expensive and laborious. (Sonar tags used on the Copper River cost $150.00 per tag.)
  Narrowband sonar can give incorrect and/or subject data. It also tends to undercount dense schools of fish because of acoustic shadowing.
Many fisheries management decisions are based on fish counts.
Resource managers need better data:
“Today we do not have adequate means of measuring the size, distribution, abundance, and passage rates of fish in the presence of man-made impediments in riverine environments.” -- (Pat Simpson, October 2000)

## Slide 6: Narrowband Sonar: Disadvantages
Sonar operators identify fish using target strength thresholds. Detections are often problematic.
Target tracks are considers equivalent to counts, but most sonar systems rely on the operator to define tracks. This is both laborious and highly subjective.
Acoustic shadowing is a problem at high fish densities:

## Slide 7: Building a Better Fish Counter:
Scientific Fishery Systems proposed development of a riverine broadband, fish tracking sonar system as a possible solution to problems with current fish tracking/counting methods:
  Technology developed for the SciFish 2000 sonar would be used to identify targets.
  Broadband sonar would offer better spatial resolution, more stable target strength measurements, and fewer problems with acoustic shadowing.
  Automated tracking would reduce labor costs while improving the objectivity of fish counts.

## Slide 8: Analysis and Design Goals
Because many tracking algorithms are computationally intensive, track computation and display needed to be fast.
  This implied that track computation had to be done in C++.
Backwards compatibility with the SciFish 2000 and code modularity were primary design and implementation goals, because this would allow us to re-use code, user documentation, testing, and test data.
  Forms and display needed to conform to the conventions used in the SciFish 2000.
  Additional code need to be as separate as possible from pre-exist code.
  Existing classes and methods could be extended, but any changes had to preserve original functionality.
  Necessary changes to the database schema had to be compatible with the SciFish 2000’s schema. Old tables couldn’t be changed. The tracker had to be able to create reasonable defaults when opening legacy databases.
Notes: Builds on existing SF2K Technology

## Slide 9: The SciFish 2000’s UI: Class Diagram
On the right is a class diagram of the SciFish 2000’s UI.
Most signal processing for the system is done in an equally complex OCX written in MS VC++.
This diagram is provided to give and indication of system complexity.
(Diagram prepared by Jennifer Gunderson, and used with her permission.)

## Slide 10: Integration Plan
An integration plan was developed. This plan was a functional and technical specification for the tracker integration.
The integration plan was formally reviewed on 6/5/2002.
At the suggestion of Jennifer Gunderson, echo caching was added to the technical specification of the plan in order to improve performance.
The amended plan (with echo caching) was accepted.

## Slide 11: Revised Dataflow: Functional View
User Interface
Tracker Settings
New Table:
TrackedEchoes
Databases
Echo Cache and Tracker Algorithm(s)
Main Displays
New Table:
Tracks
Data Flow - High Level Overview
Signal Processing (Echo Extraction)
Sonar Pings
Reports / Counts

## Slide 12: Revised Dataflow: Implementation
VB Tracker Class:
SonarClass: Access Functions
SonarOCX Access Functions
VB Side
C++ Side
Echo Cache: Stores Echo & Track Data Does “Bookkeeping”
Algorithm “X” Class Holds Algo Parameters Calculates Tracks
Parameters & Commands to Tracker
Echo Data (Ranges)
Track Associations Newly Created Tracks
Echoes
Track Info
Dapl & DSPoutput classes: Ping Processing Echo Extraction Echo Classification
Echoes
To Displays
Database
Settings Forms

## Slide 13: An Operational Example
This example shows how Tracker parameters are set, and the resulting tracks. The colored points are echoes. The narrow blue lines connecting the echoes are tracks. The scale on the right (of the echogram) is range in meters. The scale on the bottom is time/pings.
(The raw data was collected during a pool experiment in January of 2002.)

## Slide 14: Conclusion: Further Work
We will are going to develop a split-beam version of the system that would be capable of resolving and tracking targets in 3-D space. (This will entail major changes to the signal processing path.)
There are upcoming pool tests scheduled for December 14rd and 15th.
There are field tests scheduled for the summer of 2003 at sites along the Copper River.

## Slide 15: The End.
Questions???
Robert Buchanan - Email: RobertBuchanan@GCI.net - Phone: 907-338-3242